## Slide 1: Chapter 1~5 Summary

## Slide 2: General design procedure for combi. logic
1. Understand the problem
  what is the circuit supposed to do?
  write down inputs (data, control) and outputs
  draw block diagram or other picture
2. Formulate the problem using a suitable design representation
  truth table or waveform diagram are typical
  may require encoding of symbolic inputs and outputs
3. Choose implementation target
  ROM, PAL, PLA
  mux, decoder and OR-gate
  discrete gates (fixed logic)
4. Follow implementation procedure
  K-maps for two-level, multi-level
  design CAD tools and hardware description language (e.g., Verilog)
Typically, we have to separate the I/O variables and system internals to understand the problem. Step 2 is abstract representation while steps 3 and 4 are H/W implementation dependent

## Slide 3: Agenda
QM method
Hazard-free circuit design
Implementation methods: MUX, PLA, …
Number system and 4-bit/16-bit adder

## Slide 4: Design example: BCD increment by 1
I8 I4 I2 I1 O8 O4 O2 O1 0 0 0 0 0 0 0 1
0 0 0 1 0 0 1 0
0 0 1 0 0 0 1 1
0 0 1 1 0 1 0 0
0 1 0 0 0 1 0 1
0 1 0 1 0 1 1 0
0 1 1 0 0 1 1 1
0 1 1 1 1 0 0 0
1 0 0 0 1 0 0 1
1 0 0 1 0 0 0 0
1 0 1 0 X X X X
1 0 1 1 X X X X
1 1 0 0 X X X X
1 1 0 1 X X X X
1 1 1 0 X X X X
1 1 1 1 X X X X
block diagram
and
truth table
4-variable K-map for each of the 4 output functions
O1
O2 O4
O8
I1
I2 I4
I8

## Slide 5: 3.2.1 Q-M Method
Quine-McCluskey Method
an exact algorithm that reduces a minterm expression to a min. form.
can be programmed for a digital computer.
can handle more variables than K-map.
Two major steps ( a general logic minimization procedure)
  Step 1. Find all PI’s of the given minterm expression
  by repeatedly applying XY + XY’ = X
  (algebraic simplification).
  Step 2. Select a min. set of PI’s using a PI chart.
    2.1 Select EPI’s
    2.2 Select a min. # of additional non-EPIs covering the remaining 1’s.

## Slide 6: 3.2.1 Q-M Method
Step 1: Find all prime implicants
For convenience, we divide product terms in groups according to the number of 1’s in each term
group i: product terms with i 1’s.
Product terms in group i are candidates to be combined with product terms in group (i1).
group ABC Decimal
0 0 0 0 0
1 0 0 1 1
0 1 0 2
1 0 0 4
2 0 1 1 3
1 0 1 5
1 1 0 6
3 1 1 1 7
Can be combined. Futher check necessary.
Cannot be combined.
3 variables

## Slide 7: 3.2.1 Q-M Method
Example: F(A,B,C,D) = m(0,1,2,5,6,7,8,9,10,14)
COL 1 COL II COL III
0 0000
1 0001
2 0010
8 1000
5 0101
6 0110
9 1001
10 1010
7 0111
14 1110
1 0
1 1
0 1
0 1
D
A
0 1
1 1
0 0
1 1
B
C
0 4
1 5
12 8
13 9
D
A
3 7
2 6
15 11
14 10
C
B

## Slide 8: 3.2.1 Q-M Method
Example: F(A,B,C,D) = m(0,1,2,5,6,7,8,9,10,14)
COL 1 COL II COL III
0 0000 V (0,1) 000-
1 0001 V
2 0010
8 1000
5 0101
6 0110
9 1001
10 1010
7 0111
14 1110
V
(0,2) 00-0
1 0
1 1
0 1
0 1
D
A
0 1
1 1
0 0
1 1
B
C
0 4
1 5
12 8
13 9
D
A
3 7
2 6
15 11
14 10
C
B

## Slide 9: 3.2.1 Q-M Method
Example: F(A,B,C,D) = m(0,1,2,5,6,7,8,9,10,14)
COL 1 COL II COL III
0 0000 V (0,1) 000-
(0,2) 00-0
(0,8) -000
1 0001 V
2 0010 V
8 1000 V
5 0101
6 0110
9 1001
10 1010
7 0111
14 1110
Positions of ‘–’ must be same.
Two products with one-bit difference can be combined..
X
The same process can be repeated until no more combinations are possible

## Slide 10: 3.2.1 Q-M Method
Example: F(A,B,C,D) = m(0,1,2,5,6,7,8,9,10,14)
COL 1 COL II COL III
0 0000 V (0,1) 000-
(0,2) 00-0
1 0001 V (0,8) -000
2 0010 V
8 1000 V (1,5) 0-01
(1,9) –001
5 0101 V (2,6) 0-10
6 0110 V (2,10) -010
9 1001 V (8,9) 100-
10 1010 V (8,10) 10-0
7 0111 V (5,7) 01-1
14 1110 V (6,7) 011-
(6,14) -110
(10,14) 1-10
(0,1,8,9) -00-
V
1 0
1 1
0 1
0 1
D
A
0 1
1 1
0 0
1 1
B
C

## Slide 11: 3.2.1 Q-M Method
Example: F(A,B,C,D) = m(0,1,2,5,6,7,8,9,10,14)
COL 1 COL II COL III
0 0000 V (0,1) 000-
(0,2) 00-0
1 0001 V (0,8) -000
2 0010 V
8 1000 V (1,5) 0-01
(1,9) –001
5 0101 V (2,6) 0-10
6 0110 V (2,10) -010
9 1001 V (8,9) 100-
10 1010 V (8,10) 10-0
7 0111 V (5,7) 01-1
14 1110 V (6,7) 011-
(6,14) -110
(10,14) 1-10
(0,1,8,9) -00-
V
1 0
1 1
0 1
0 1
D
A
0 1
1 1
0 0
1 1
B
C
Cube is Expanded!

## Slide 12: 3.2.1 Q-M Method
Example: F(A,B,C,D) = m(0,1,2,5,6,7,8,9,10,14)
COL 1 COL II COL III
0 0000 V (0,1) 000- V (0,1,8,9) -00-
(0,2) 00-0 V (0,2,8,10) -0-0
1 0001 V (0,8) -000 V (0,8,1,9) -00-
2 0010 V (0,8,2,10) -0-0
8 1000 V (1,5) 0-01
(1,9) –001 V (2,6,10,14) - -10
5 0101 V (2,6) 0-10 V (2,10,6,14) - -10
6 0110 V (2,10) -010 V
9 1001 V (8,9) 100- V
10 1010 V (8,10) 10-0 V
7 0111 V (5,7) 01-1
14 1110 V (6,7) 011-
(6,14) -110 V
(10,14) 1-10 V
1 0
1 1
0 1
0 1
D
A
0 1
1 1
0 0
1 1
B
C

## Slide 13: 3.2.1 Q-M Method
Example: F(A,B,C,D) = m(0,1,2,5,6,7,8,9,10,14)
COL 1 COL II COL III
0 0000 V (0,1) 000- V (0,1,8,9) -00-
(0,2) 00-0 V (0,2,8,10) -0-0
1 0001 V (0,8) -000 V (0,8,1,9) -00-
2 0010 V (0,8,2,10) -0-0
8 1000 V (1,5) 0-01
(1,9) –001 V (2,6,10,14) - -10
5 0101 V (2,6) 0-10 V (2,10,6,14) - -10
6 0110 V (2,10) -010 V
9 1001 V (8,9) 100- V
10 1010 V (8,10) 10-0 V
7 0111 V (5,7) 01-1
14 1110 V (6,7) 011-
(6,14) -110 V
(10,14) 1-10 V
-00-
-0-0
redundant
redundant
- -10
redundant
0-01
01-1
011-

## Slide 14: 3.2.1 Q-M Method
5. Mark product terms that were combined to reduce.
These are not PI’s.
6. - represents a disappeared variable.
7. When COL II  COL III, two terms cannot be combined if they
have ‘-’ at different positions. Ex: 000- + 0-10  A’B’C’ + A’CD’
8. Remaining unmarked product terms are PI’s: 6 PI’s.
COL III COL II
  F = B’C’ + B’D’ + CD’ + A’C’D + A’BD + A’BC
9. Above expression is not a min. form, but a collection of PI’s.
  Min. form : F = B’C’ + CD’ + A’BD
  We use a prime implicant chart to find EPI’s from the above PI’s.

## Slide 15: 3.2.1 Q-M Method
  6 PI’s: B’C’ + B’D’ + CD’ + A’C’D + A’BD + A’BC
Prime Minterms
Implicants 0 1 2 5 6 7 8 9 10 14
0,1,8,9 B’C’ x x x x
0,2,8,10 B’D’ x x x x
2,6,10,14 CD’ x x x x
1,5 A’C’D x x
5,7 A’BD x x
6,7 A’BC x x
  Step 2: Select a min. set of PI’s using a Prime Implicant Chart
1st column = prime implicants
Other columns = ON-set elements covered by each PI
0 4
1 5
12 8
13 9
D
A
3 7
2 6
15 11
14 10
C
B

## Slide 16: 3.2.1 Q-M Method
  Method 1: Find EPI, remembering that, if a minterm is covered by only one PI, that PI is EPI.
Step 2: Select a min. set of PI’s using a Prime Implicant Chart
EPI=Essential Prime Implicant
distinguished 1-cell
distinguished 1-cell
Prime Minterms
Implicants 0 1 2 5 6 7 8 9 10 14
0,1,8,9 B’C’ x x x x
0,2,8,10 B’D’ x x x x
2,6,10,14 CD’ x x x x
1,5 A’C’D x x
5,7 A’BD x x
6,7 A’BC x x
B’C’

## Slide 17: 3.2.1 Q-M Method
  Method 1: Find EPI, remembering that, if a minterm is covered by only one PI, that PI is EPI.
Step 2: Select a min. set of PI’s using a Prime Implicant Chart
EPI=Essential Prime Implicant
distinguished 1-cell
distinguished 1-cell
Prime Minterms
Implicants 0 1 2 5 6 7 8 9 10 14
0,1,8,9 B’C’ x x x x
0,2,8,10 B’D’ x x x x
2,6,10,14 CD’ x x x x
1,5 A’C’D x x
5,7 A’BD x x
6,7 A’BC x x
B’C’
CD’
The min. form, F = B’C’ + CD’ + A’BD
A’BD

## Slide 18: 3.2.1 Q-M Method
Don’t care terms
  We can handle don’t care terms as if we handle them on a K-map.
Q-M method with Don’t cares
Step 1: Finding all PI’s (as usual)
Step 2: Selecting a minimum number of PI’s covering all minterms.
  Hide don’t cares on the PI chart
  Do as usual
1 0
1 1
0 X
0 1
D
A
0 X
1 X
0 0
1 1
B
C
1 0
1 1
0 1
0 1
D
A
0 1
1 1
0 0
1 1
B
C
Notes: Ana’logous

## Slide 19: 3.2.1 Q-M Method
Minterms
0 1 2 5 6 7 8 9 10 14
0,1,8,9 B’C’ x x x x
0,2,8,10 B’D’ x x x x
2,6,10,14 CD’ x x x x
1,5 A’C’D x x
5,7 A’BD x x
6,7 A’BC x x
Prime Implicant Chart with don’t care terms
Assume that minterms 6, 7, and 8 are don’t care terms.
  We don’t need to show them on a PI chart, and they can be hidden.

## Slide 20: 3.2.1 Q-M Method
Minterms
0 1 2 5 6 7 8 9 10 14
0,1,8,9 B’C’ x x x x
0,2,8,10 B’D’ x x x x
2,6,10,14 CD’ x x x x
1,5 A’C’D x x
5,7 A’BD x x
6,7 A’BC x x
Prime Implicant Chart with don’t care terms
Assume that minterms 6, 7, and 8 are don’t care terms.
  We don’t need to show them on a PI chart, and they can be hidden.

## Slide 21: 3.2.1 Q-M Method
Minterms
0 1 2 5 6 7 8 9 10 14
0,1,8,9 B’C’ x x x x
0,2,8,10 B’D’ x x x x
2,6,10,14 CD’ x x x x
1,5 A’C’D x x
5,7 A’BD x x
6,7 A’BC x x
Prime Implicant Chart with don’t care terms
Assume that minterms 6, 7, and 8 are don’t care terms.
  We don’t need to show them on a PI chart, and they can be hidden.
The min. form, F = B’C’ + CD’ + A’BD

## Slide 22: 2-input AND Gate is More Expensive than 2-input NAND Gate
2-input NAND gate
Inverter
A
B
Out
Out
2-input AND gate

## Slide 23: Two-level logic using NAND gates (cont’d)
OR gate with inverted inputs is a NAND gate
  de Morgan’s: A’ + B’ = (A • B)’
Two-level NAND-NAND network
  inverted inputs are not counted
  in a typical circuit, inversion is done once and signal distributed
Recall de Morgan’s Law. When inverters are passing through a gate, the gate should be changed from OR to AND and vice versa.

## Slide 24: Agenda
QM method
Hazard-free circuit design
Implementation methods: MUX, PLA, …
Number system and 4-bit/16-bit adder

## Slide 25: 3.5 Time Response in Combinational Networks
Static 1-Hazard
Without the notion of time, we can safely A+A’=1
Static 1-Hazard happens as A+A’  1 momentarily.
I.e., A=A’=0 momentarily.
IMPORTANT: When do we have the term (A+A’) in an expression?
  Normally, it can occur in the S-O-P (AND-OR) implementation.
    F = (XXXXA) + (YYYYA’) = A+A’
1 1
Don’t use A+A’=1, when investigating the static 1-hazard. (For this purpose, A and A’ are independent variables.)
Static
1-hazard
1
1
0
Two necessary conditions of glitch:
multiple paths and different path delay
Notes: In the properly designed SOP, XX.. is not in the form of AA’… Thus, in SOP, no static 0-hazard…
In the properly designed POS, X+X.. is not in the form of A+A’… Thus, in POS, no static 1-hazard…

## Slide 26: 3.5 Time Response in Combinational Networks
Static 0-Hazard
Without the notion of time, we can safely AA’=0
Static 0-Hazard happens as AA’  0 momentarily.
I.e., A=A’=1 momentarily.
IMPORTANT: When do we have the term (AA’) in an expression?
  Normally, it can occur in the P-O-S (OR-AND) implementation.
    F = (X+X+X+A) (Y+Y+Y+A’) = AA’
0 0
Don’t use AA’=0, when investigating the static 0-hazard. (For this purpose, A and A’ are independent variables.)
Static
0-hazard
1
0
0
Notes: In the properly designed SOP, XX.. is not in the form of AA’… Thus, in SOP, no static 0-hazard…
In the properly designed POS, X+X.. is not in the form of A+A’… Thus, in POS, no static 1-hazard…

## Slide 27: 3.5 Time Response in Combinational Networks
CASE 1 ()
Input change within product term
e.g., 1100  1101
  D: 0  1
ABCD = 1100
ABCD = 1101
AB
00
01
11
10
0
0
1
1
1
1
1
1
1
1
0
0
0
0
0
0
00
01
11
10
CD
1
A
\C
\A
D
F
A
\C
\A
D
F
1
1
1
1
0
0
1
1
1
1
0
0
0
Static 1-Hazard (AND-OR circuit)
Min. S-O-P : F = A’D + AC’
Observation: F remains at ‘1’, and no glitch is generated.
It is because signal changes on a single path from input to output

## Slide 28: 3.5 Time Response in Combinational Networks
Static 1-Hazard: F = A’D + AC’
CASE 2 ()
Input change that spans product terms,
e.g, 1101  0101
AB
00
01
11
10
0
0
1
1
1
1
1
1
1
1
0
0
0
0
0
00
01
11
10
CD
0
ABCD = 1101
(A=1, A’=0)
ABCD = 0101
(A=0,A’=0)
ABCD = 0101
(A=0,A’=1)
A
\C
\A
D
F
A
\C
\A
D
F
0
1
0
0
1
0
0
1
1
1
1
1
0
0
A
\C
\A
D
F
0
1
0
1
1
1
1
  A: 1  0
A and A’:
  Assume that A changes earlier than A’
Observation: A glitch is generated (static 1-hazard).
It satisfies two necessary conditions of glitch: multiple paths and different path delay
Notes: A가 바뀌고 A’이 늦게 바뀜

## Slide 29: 3.5 Time Response in Combinational Networks
In order to eliminate the static 1-hazard,
  we need to implement F = A'D + AC' + C'D
  instead of F = A'D + AC'.
1. Path delay adjustment/matching can eliminate glitches.
2. However,
General Strategy: add redundant terms.
A
AB
00
01
11
10
0
0
1
1
1
1
1
1
1
1
0
0
0
0
0
0
00
01
11
10
C
CD
D
B
Glitch elimination methods
Two necessary conditions of glitch: multiple paths and different path delay
+ early changing input needs to change the output
This one is not satisfied
due to C’D
Notes: Why hazard free by adding C’D?
C’=D=1때만 1-0-1 glitch 가능. 하지만 이때 last term makes F=1.
Two adjacent minterms must be covered by the same product.

## Slide 30: Agenda
QM method
Hazard-free circuit design
Implementation methods: MUX, PLA, …
Number system and 4-bit/16-bit adder

## Slide 31: Multiplexers (MUXs)/selectors
two alternative forms
for a 2:1 Mux truth table
logical form
A Z 0 I0 1 I1
I1 I0 A Z 0 0 0 0 0 0 1 0 0 1 0 1 0 1 1 0 1 0 0 0 1 0 1 1 1 1 0 1 1 1 1 1
Z = A' I0 + A I1
Multiplexers/selectors: general concept
  2n data inputs, n control inputs (called "selects"), 1 output
  used to connect 2n points to a single point
  control signal pattern forms binary index of input connected to output
functional form
Let’s look at how a MUX function can be described as a boolean expression or a truth table. We will start with the simplest one, 2:1 MUX. There are two inputs I0 and I1 and the control input is A. Then Z will select I0 or I1 depending on A’s value. If we tabulate all the cases of I0 and I1, the final truth table is the one on the right.

## Slide 32: Multiplexers/selectors (cont'd)
2 -1
I0 I1 I2 I3 I4 I5 I6 I7
A B C
8:1 mux
Z
I0 I1 I2 I3
A B
4:1 mux
Z
I0 I1
A
2:1 mux
Z
k=0
n
2:1 mux: Z = A'I0 + AI1
4:1 mux: Z = A'B'I0 + A'BI1 + AB'I2 + ABI3
8:1 mux: Z = A'B'C'I0 + A'B'CI1 + A'BC'I2 + A'BCI3 + AB'C'I4 + AB'CI5 + ABC'I6 + ABCI7
In general: Z =  (mkIk)
  in minterm shorthand form for a 2n:1 Mux
How can we express the output in a general form, regardless of the # of inputs? First of all, n is the # of control wires. So there are total 2**n inputs. Here m_k is the k-th minterm from the control variables.

## Slide 33: Multiplexers as general-purpose logic (cont’d)
Generalization
Example: G(A,B,C,D) can be realized by an 8:1 MUX
n-1 mux control variables
  single mux data variable
four possible
configurations of truth table rows can be expressed as a function of In-1
I0 I1 . . . In-2 In-1 F . . . . 0 0 0 1 1 . . . . 1 0 1 0 1 0 In-1 In-1' 1
choose A,B,C as control variables
C
A
B
0 1 2 3 4 5 6 7
1 D 0 1 D’ D D’ D’
S2
8:1 MUX
S1
S0
A B C D G 0 0 0 0 1 0 0 0 1 1 0 0 1 0 0 0 0 1 1 1 0 1 0 0 0 0 1 0 1 0 0 1 1 0 1 0 1 1 1 1 1 0 0 0 1 1 0 0 1 0 1 0 1 0 0 1 0 1 1 1 1 1 0 0 1 1 1 0 1 0 1 1 1 0 1 1 1 1 1 0
1
D 0 1
D' D D’ D’
Here is the generalized n-input logic function by a (n-1)-input MUX.
Depending on the output of two cases of the singled-out variable, a different data input is attached to each minterm of the (n-1) input MUX. Reducing the MUX size is economical.

## Slide 34: Formalize the problem
C0 C1 C2 A B F
0 0 0 0 0 1
0 0 0 0 1 1
0 0 0 1 0 1
0 0 0 1 1 1
0 0 1 0 0 0
0 0 1 0 1 1
0 0 1 1 0 1
0 0 1 1 1 1
0 1 0 0 0 1
0 1 0 0 1 1
0 1 0 1 0 1
0 1 0 1 1 0
0 1 1 0 0 0
0 1 1 0 1 1
0 1 1 1 0 1
0 1 1 1 1 0
1 0 0 0 0 1
1 0 0 0 1 0
1 0 0 1 0 0
1 0 0 1 1 1
1 0 1 0 0 0
1 0 1 0 1 0
1 0 1 1 0 0
1 0 1 1 1 1
1 1 0 0 0 1
1 1 0 0 1 0
1 1 0 1 0 0
1 1 0 1 1 0
1 1 1 0 0 0
1 1 1 0 1 0
1 1 1 1 0 0
1 1 1 1 1 0
choose implementation technology 5-variable K-map to discrete gates multiplexer implementation
1 0
A B
A B
A B
C2
C0
C1
0 1 2 3 4 5 6 7
S2
8:1 MUX
S1
S0
F
In order to realize the multi-purpose function, we combine discrete gates and an 8:1 MUX.

## Slide 35: Demultiplexers as general-purpose logic (cont’d)
F1
F2
F3
F1 = A'BC'D + A'B'CD + ABCD
F2 = ABC'D' + ABC
F3 = (A' + B' + C' + D')
A
B
0 A'B'C'D' 1 A'B'C'D 2 A'B'CD' 3 A'B'CD 4 A'BC'D' 5 A'BC'D 6 A'BCD' 7 A'BCD 8 AB'C'D' 9 AB'C'D 10 AB'CD' 11 AB'CD 12 ABC'D' 13 ABC'D 14 ABCD' 15 ABCD
4:16 DEC
Enable
C
D
By using a single 4:16 DEMUX, we can implement three functions of 4 variables, with a few more gates.
DEMUX is a minterm generator!

## Slide 36: Programmable logic arrays (PLAs)
• • •
inputs
AND array
• • •
outputs
OR array
product terms
Pre-fabricated building block of many AND/OR gates
  actually NOR or NAND
  "personalized" by making/breaking connections among the gates
  programmable array block diagram for sum of products form
A PLA is a general implementation of sum of products of a logic function. We first implement each product term (not necessarily minterm). Then the product terms will be Ored in the next stage. So we have two generic logic arrays. Programming means configuring connections in two arrays.
Sum of
products

## Slide 37: Before programming
All possible connections are available before "programming"
  in reality, all AND and OR gates are NANDs
We have to look at two cross-connects: one is between inputs and AND gates and the other is between AND gates and OR gates. We can make or break connections in those two cross-connects.
AB
A
B
C

## Slide 38: After programming
A
B
C
F1
F2
F3
F0
AB
B'C
AC'
B'C'
A
Unwanted connections are "blown"
  fuse (normally connected, break unwanted ones)
  anti-fuse (normally disconnected, make wanted connections)
Then we have to do programming, which is the process of enabling or disabling each cross-point. If fuses are used for each cross point, we break unwanted ones. If anti-fuses are used, we enable the wanted ones.

## Slide 39: PLA example
A B C F1 F2 F3 F4 F5 F6
0 0 0 0 0 1 1 0 0
0 0 1 0 1 0 1 1 1
0 1 0 0 1 0 1 1 1
0 1 1 0 1 0 1 0 0
1 0 0 0 1 0 1 1 1
1 0 1 0 1 0 1 0 0
1 1 0 0 1 0 1 0 0
1 1 1 1 1 0 0 1 1
A'B'C'
A'B'C
A'BC'
A'BC
AB'C'
AB'C
ABC'
ABC
A
B
C
F1
F2
F3
F4
F5
F6
full decoder as for memory address
bits stored in memory
Multiple functions of A, B, C
  F1 = A B C
  F2 = A + B + C
  F3 = A' B' C'
  F4 = A' + B' + C'
  F5 = A xor B xor C
  F6 = A xnor B xnor C
Here are the six functions of three variables.
As there are three variables, total 8 minterms exist. Then all the relevant minterms of each function will be connected to its OR gate.

## Slide 40: Agenda
QM method
Hazard-free circuit design
Implementation methods: MUX, PLA, …
Number system and 4-bit/16-bit adder

## Slide 41: Number systems
Representation of positive numbers is the same in most systems
Major differences are in how negative numbers are represented
Representation of negative numbers come in three major schemes
  sign and magnitude
  1s complement
  2s complement
Assumptions
  we'll assume a 4 bit machine word
  16 different values can be represented
  roughly half are positive, half are negative
To design arithmetic functions, we have to understand how a number is represented in computers. We talked about binary coding, BCD coding and so on. Here we choose the binary coding as the basic representation system but will focus on how negative numbers are expressed.
For the purpose of illustration, we consider the case of using 4 wires to represent a digit (positive and negative and zero).

## Slide 42: 2s complement
0 100 = + 4 1 100 = – 4
+0
+1
+2
+3
+4
+5
+6
+7
–8
–7
–6
–5
–4
–3
–2
–1
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
1s complement with negative numbers shifted one position clockwise
  only one representation for 0
  one more negative number than positive numbers
  high-order bit can act as sign bit
2s compliment enhances the 1s complement encoding, it can represent up to -8 as shown in the above.

## Slide 43: Full adder implementations
Cout = A B + Cin (A xor B) = A B + Cin (A or B)
A
B
Cin
S
A
A
B
B
Cin
Cout
A
B
A xor B
Cin
A xor B xor Cin
Half Adder
Sum
Cout
Cin (A xor B)
A B
Cout
Half Adder
Sum
Cout
At the top, there is a fixed logic implementation of a full adder. If we use two half-adder modules to construct the full-adder system instead of using random logic, we can reduce the number of gates.
Standard approach
  6 gates
  2 XORs, 2 ANDs, 2 ORs
Alternative implementation
  5 gates
  half adder is an XOR gate and AND gate
  2 XORs, 2 ANDs, 1 OR

## Slide 44: Adder/subtractor
Now we have a full adder for one bit addition. Then what we want to do is addition/subtraction of two 4bit-numbers. Addition is easy. Recall that 2s complement of a number is its inverted form+1. So we can use the same adding function to perform subtraction too. For subtraction, we just enable the control input.
A
B
Cout
Sum
Cin
0
1
Add' Subtract
A0
B0
B0'
Sel
Overflow
A
B
Cout
Sum
Cin
A1
B1
B1'
Sel
A
B
Cout
Sum
Cin
A2
B2
B2'
Sel
0
1
0
1
0
1
A
B
Cout
Sum
Cin
A3
B3
B3'
Sel
S3
S2
S1
S0
Use an adder to do subtraction thanks to 2s complement representation
  A – B = A + (– B) = A + B' + 1
  control signal selects B or 2s complement of B

## Slide 45: Ripple-carry adders
A
A
B
B
Cin
Cout
@0
@0
@0
@0
@N
@1
@1
@N+1
@N+2
late
arriving
signal
two gate delays
to compute Cout
4 stage
adder
A0
B0
0
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
Critical delay
  the propagation of carry from low to high order stages
The next advanced adder is a ripple-carry adder. What is the problem of the full adder in the previous slide? When we consider data bits, they are coming in parallel at the same time. However, carries should be cascaded with delays proportional to the bit positions. On the left, Cin comes at time N, then Cout will be valid at time N+2 (each one-bit adder incurs 2 gate delays)
1111+0001
A
B
Cin
S

## Slide 46: Carry-lookahead logic
Carry generate: Gi = Ai Bi
  must generate carry when A = B = 1
Carry propagate: Pi = Ai xor Bi
  carry-in will equal carry-out here
Sum and Cout can be re-expressed in terms of generate/propagate:
  Si = Ai xor Bi xor Ci = Pi xor Ci
  Ci+1 = Ai Bi + Ai Ci + Bi Ci = Ai Bi + Ci (Ai + Bi) = Ai Bi + Ci (Ai xor Bi) = Gi + Ci Pi
Instead of awaiting the carry from the lower-order bits, we can process the carry in advance. How?
In order to do so, the carry should be derived from the lower-order data bits directly. First of all, let’s look at two new functions: Gi and Pi. Then Si and Ci+1 can be rewritten as shown in the above. Actually, those imply two cases. When Gi is true, there is always a carry-out. If Pi is true, a carry-out depends on a carry-in.

## Slide 47: Carry-lookahead logic (cont’d)
Re-express the carry logic as follows:
  C1 = G0 + P0 C0
  C2 = G1 + P1 C1 = G1 + P1 G0 + P1 P0 C0
  C3 = G2 + P2 C2 = G2 + P2 G1 + P2 P1 G0 + P2 P1 P0 C0
  C4 = G3 + P3 C3 = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0 + P3 P2 P1 P0 C0
Each of the carry equations can be implemented with two-level logic
  all inputs are now directly derived from data inputs and not from intermediate carries
  this allows computation of all sum outputs to proceed in parallel
Then all the carries are calculated by the expanding Pi and Gi as shown in the above, which is called the carry-lookahead logic. Note that all carries are now just two-level logic functions. So here is the bottom line: there is a tradeoff between the number of gates and the delay.

## Slide 48: Carry-lookahead (CLA) implementation
G3
C0
C0
C0
C0
P0
P0
P0
P0
G0
G0
G0
G0
C1 @ 3
P1
P1
P1
P1
P1
P1
G1
G1
G1
C2 @ 3
P2
P2
P2
P2
P2
P2
G2
G2
C3 @ 3
P3
P3
P3
P3
C4 @ 3
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
increasingly complex logic for carries
Adder with propagate and generate outputs
This slide shows how 4 carries are implemented in two level fixed logic based on Pi and Gi. As Pi and Gi take only one gate delay, the final carries take maximum 3 gate delays.

## Slide 49: Building Blocks of Carry Lookahead Adder
G3
C0
C0
C0
C0
P0
P0
P0
P0
G0
G0
G0
G0
C1
P1
P1
P1
P1
P1
P1
G1
G1
G1
C2
P2
P2
P2
P2
P2
P2
G2
G2
C3
P3
P3
P3
P3
C4
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
1b Adder
Ai
Bi
Ci
Pi
Si
Gi
4b Carry Lookahead logic
C0
C1
P0
G0
P1
G1
P2
G2
P3
G3
C2
C3
C4
Delay of Ci is 3 time units (=P/G gen 1 + C gen 2)
Delay of C0 to Si is 3 time units.

## Slide 50: 4-bit Carry Lookahead Adder
1b Adder
A0
B0
C0
P0
S0
G0
4b Carry Lookahead logic
C0
C1
P0
G0
P1
G1
P2
G2
P3
G3
C2
C3
C4
1b Adder
A1
B1
C1
P1
S1
G1
1b Adder
A2
B2
C2
P2
S2
G2
1b Adder
A3
B3
C3
P3
S3
G3
4b Carry Lookahead Adder
C0
S0
A0
B0
S1
S2
S3
B1
B2
B3
A1
A2
A3
C4
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
Assuming A, B and C0 arrive at time 0
For all i >=1
Delay of Si = 1 + delay of Ci = 4

## Slide 51: CLA implementation (cont’d)
on the left, there is the original full adder, which takes a long time to finish addition. On the right, there is the carry lookahead adder. The two level logic functions for carries are not shown. Each box is the one-bit adder module. Overall, by using a lot of gates for CLA in the previous slide, we can reduce the delay of the addition process.
A0
B0
0
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
A0
B0
0
S0 @2
A1
B1
C1 @3
S1 @4
A2
B2
C2 @3
S2 @4
A3
B3
C3 @3
S3 @4
C4 @3
C4 @3
Carry-lookahead logic generates individual carries
  sums computed much more quickly in parallel
  however, cost of carry logic increases with more stages

## Slide 52: 16bit CLA adder with cascaded carry-lookahead logic
Carry-lookahead (CLA) adder
  4 four-bit adders with internal carry lookahead
  second level carry lookahead unit extends lookahead to 16 bits
If we add 16bit long numbers, we have to use 4 4bit CLA adder modules. Each module adds 4 bits. Here Ci at the bottom box is the carry from the i-th 4bit CLA adder module. Pi and Gi in blue color are the same functions in the previous example. While Pi and Gi at the bottom unit give info about the carries between the 4bit CLA modules, which is more complicated.
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@5
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
G = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0
P = P3 P2 P1 P0
C1 = G0 + P0 C0
C2 = G1 + P1 G0 + P1 P0 C0

## Slide 53: Agenda
QM method
Hazard-free circuit design
Implementation methods: MUX, PLA, …
Number system and 4-bit/16-bit adder

## Slide 54: Summary Part 2 Sequential circuit design

## Slide 55: Overview
D F/F, register, and counter
Finite state machine design
State minimization
Design examples

## Slide 56: Timing constraints
Definition of terms
  clock: periodic event, causes state of memory element to change can be rising edge or falling edge or high level or low level
  setup time: minimum time before the clocking event by which the input must be stable (Tsu)
  hold time: minimum time after the clocking event until which the input must remain stable (Th)
Let’s go over terminologies first. We already know what is a clock. For each edge of a clock signal, there are some timing constraints. Suppose the positive edge of a clock signal triggers a circuit. Then the data input should be stable for an interval which is Tsu+Th, which are dependent on transistor circuit delay.
there is a timing "window" around
the clocking event during which the
input must remain stable and
unchanged in order to be recognized
clock
data
changing
stable
input
clock
Tsu
Th
clock
data
D
Q

## Slide 57: Cascading Edge-triggered Flip-Flops
IN
Q0
Q1
CLK
100
Shift register
  New value goes into first stage
  While previous value of first stage goes into second stage
  Consider setup/hold/propagation delays (Tpd must be > Th)
CLK
IN
Q0
Q1
D
Q
D
Q
OUT

## Slide 58: Universal shift register
clear sets the register contents and output to 0 s1 and s0 determine the shift function s0 s1 function 0 0 hold state 0 1 shift right 1 0 shift left 1 1 load new input
left_in
left_out
right_out
clear
right_in
output
input
s0
s1
clock
Holds 4 values
  serial or parallel inputs
  serial or parallel outputs
  permits shift left or right
  shift in new values from left or right
The shift register in the previous slide goes only from left to right. Here we want to design a generic or multi-purpose shift register with the above functionalities. In addition, we also want to hold the current value without I/O. Overall, we need some control variables.

## Slide 59: Design of universal shift register
Nth cell
D
Q
CLK
Q[N-1] (left)
Q[N+1] (right)
Input[N]
to N-1th cell
to N+1th cell
clear s0 s1 new value 1 – – 0 0 0 0 output (hold) 0 0 1 output value of left FF (shift right) 0 1 0 output value of right FF(shift left) 0 1 1 input (load)
Consider one of the four flip-flops
  new value at next clock cycle:
s0 and s1 control mux
0
1
2
3
CLEAR
Each memory module (that stores 1 bit) should be able to perform 5 functions. Note that there are multiple incoming lines and one of them should be selected. This should ring the bell. It will be convenient to use a MUX. Blue wires are about control while black wires are data paths. Here, clear, S1 and S0 are depicted by a single wire for simplicity.
CLK
clear, s0, s1

## Slide 60: Pattern recognizer
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
OUT
Combinational function of input samples
  in this case, recognizing the pattern 1001 on the single input signal
Another useful application of shift registers is bit string identification. In this case, bits are shifted from left to right. At any moment, if 4 bits are 1001, then OUT will be true.

## Slide 61: Four-bit binary synchronous up-counter
EN D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
(1) Low order 4-bits = 1111
(2) RCO goes high
(3) High order 4-bits are incremented
Standard component with many applications
  positive edge-triggered FFs w/ synchronous load and clear inputs
  parallel load data from D, C, B, A
  enable inputs: must be asserted to enable counting
  ripple-carry out (RCO) is used for cascading counters
    high when counter is in its highest state 1111
    implemented using an AND gate
If we use the binary counter in the previous slide as a basic component, we can build many complicated circuits, e.g. a wider binary counter. Here D is the MSB.
Preset
logic

## Slide 62: Offset counters
Starting offset counters – use of synchronous load
  e.g., 0110, 0111, 1000, 1001, 1010, 1011, 1100, 1101, 1111, 0110, . . .
Ending offset counter – comparator for ending value
  e.g., 0000, 0001, 0010, ..., 1100, 1101, 0000
Combinations of the above (start and stop value)
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "0" "0" "0"
"0"
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "1" "1" "0"
Other examples are here; using the load input, we can control the initial value. Or by using some product term from the stored values, we can configure the ending value of the counter.

## Slide 63: Overview
D F/F, register, and counter
Finite state machine design
State minimization
Design examples

## Slide 64: State Diagram to Encoded State Transition Table
010
100
110
011
001
000
101
111
3-bit up-counter
current state next state 0 000 001 1 1 001 010 2 2 010 011 3 3 011 100 4 4 100 101 5 5 101 110 6 6 110 111 7 7 111 000 0
Tabular form of state diagram
Like a truth-table (specify output for all input combinations)
Encoding of states: easy for counters – just use value

## Slide 65: Implementation
C3 C2 C1 N3 N2 N1 0 0 0 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 0 1 0 1 1 0 1 1 1 0 1 1 0 1 1 1 1 1 1 0 0 0
N1 := C1'
N2 := C1C2' + C1'C2
:= C1 xor C2
N3 := C1C2C3' + C1'C3 + C2'C3
:= C1C2C3' + (C1' + C2')C3
:= (C1C2) xor C3
notation to show
function represent input to D-FF
D flip-flop for each state bit
Combinational logic based on encoding
0 0
0 1
1 1
0 1
C1
C2
C3
N3
0 1
1 0
1 0
0 1
C1
C2
C3
N2
1 1
0 0
1 1
0 0
C1
C2
C3
N1

## Slide 66: Implementation
Current state = D F/F outputs
Next state = D F/F inputs
C3 C2 C1 N3 N2 N1 0 0 0 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 0 1 1 1 0 0 1 0 0 1 0 1 1 0 1 1 1 0 1 1 0 1 1 1 1 1 1 0 0 0
N1 := C1'
N2 := C1C2' + C1'C2
:= C1 xor C2
N3 := C1C2C3' + C1'C3 + C2'C3
:= C1C2C3' + (C1' + C2')C3
:= (C1C2) xor C3
notation to show
function represent input to D-FF
D
Q
D
Q
D
Q
C1
C2
C3
CLK
"1"
N1
N2
N3

## Slide 67: More Complex Example
Complex Counter
  Repeats five states in sequence
  Not a binary number representation
Step 1: Derive the state transition diagram
  Count sequence: 000, 010, 011, 101, 110
Step 2: Derive the state transition table from the state transition diagram
Present State Next State
C B A C+ B+ A+
0 0 0 0 1 0
0 0 1 – – –
0 1 0 0 1 1
0 1 1 1 0 1
1 0 0 – – –
1 0 1 1 1 0
1 1 0 0 0 0
1 1 1 – – –
note the don't care conditions that arise from the unused state codes
010
000
110
101
011

## Slide 68: More Complex Counter Example (cont’d)
Step 3: K-maps for Next State Functions
C+ := A
B+ := B' + A'C'
A+ := BC'
0 0
X 1
0 X
X 1
A
B
C
C+
1 1
X 0
0 X
X 1
A
B
C
B+
0 1
X 1
0 X
X 0
A
B
C
A+
D
Q
D
Q
D
Q
C
B
A
CLK
C+
B+
A+
Some logic here!

## Slide 69: Self-Starting Counters (cont’d)
Re-deriving state transition table from don't care assignment
0 0
1 1
0 0
1 1
A
B
C
C+
1 1
1 0
0 1
0 1
A
B
C
B+
0 1
0 1
0 0
0 0
A
B
C
A+
Present State Next State
C B A C+ B+ A+
0 0 0 0 1 0
0 0 1 1 1 0
0 1 0 0 1 1
0 1 1 1 0 1
1 0 0 0 1 0
1 0 1 1 1 0
1 1 0 0 0 0
1 1 1 1 0 0
010
000
110
101
011
001
111
100

## Slide 70: Overview
D F/F, register, and counter
Finite state machine design
State minimization
Design examples

## Slide 71: Example: Vending Machine
Vending Machine FSM
N
D
Reset
Clock
Open
Coin Sensor
Release Mechanism
Release item after 15 cents are deposited
Single coin slot for dimes (10 cents), nickels (5 cents)
No change

## Slide 72: Example: Vending Machine
Suitable Abstract Representation
  Tabulate typical input sequences:
    3 nickels
    nickel, dime
    dime, nickel
    two dimes
  Draw state diagram:
    Inputs: N, D, reset
    Output: open chute
  Assumptions:
    Assume N and D asserted for one cycle
    Each state has a self loop for N = D = 0 (no coin)
S0
Reset
S2
D
S6
[open]
D
S4
[open]
D
S1
N
S3
N
S7
[open]
N
S5
[open]
N

## Slide 73: Example: Vending Machine
State Diagram
S0
Reset
S2
D
S6
[open]
D
S4
[open]
D
S1
N
S3
N
S7
[open]
N
S5
[open]
N
present inputs next output state D N state open S0 0 0 S0 0 0 1 S1 0 1 0 S2 0 1 1 – – S1 0 0 S1 0 0 1 S3 0 1 0 S4 0 1 1 – – S2 0 0 S2 0 0 1 S5 0 1 0 S6 0 1 1 – – S3 0 0 S3 0 0 1 S7 0 1 – – – S4 – – S4 1 S5 – – S5 1 S6 – – S6 1 S7 – – S7 1
symbolic state table

## Slide 74: Example: Vending Machine
State Encoding and Truth Table
Present state inputs next state output Q2 Q1 Q0 D N D2 D1 D0 open 0 0 0 0 0 0 0 0 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 – – – – 0 0 1 0 0 0 0 1 0 0 1 0 1 1 0 1 0 1 0 0 0 1 1 – – – – 0 1 0 0 0 0 1 0 0 0 1 1 0 1 0 1 0 1 1 0 0 1 1 – – – – 0 1 1 0 0 0 1 1 0 0 1 1 1 1 0 1 – – – – – 1 0 0 – – 1 0 0 1 1 0 1 – – 1 0 1 1 1 1 0 – – 1 1 0 1 1 1 1 – – 1 1 1 1

## Slide 75: Example: Vending Machine
Implementation: D2, D1, D0, Open
D2 = Q2 + Q0·D + Q1·N + Q1·D
Open = Q2

## Slide 76: Example: Vending Machine
Implementation: D2
Current state = D F/F outputs
Next state = D F/F inputs

## Slide 77: Example: Vending Machine
Implementation: D1
Current state = D F/F outputs
Next state = D F/F inputs

## Slide 78: Example: Vending Machine
Implementation: D0
Current state = D F/F outputs
Next state = D F/F inputs

## Slide 79: Example: Vending Machine
Implementation: Open
13 gates + 3 F/Fs

## Slide 80: Example: Vending Machine (cont’d)
Minimize number of states - reuse states whenever possible
symbolic state table
present inputs next output state D N state open 0¢ 0 0 0¢ 0 0 1 5¢ 0 1 0 10¢ 0 1 1 – – 5¢ 0 0 5¢ 0 0 1 10¢ 0 1 0 15¢ 0 1 1 – – 10¢ 0 0 10¢ 0 0 1 15¢ 0 1 0 15¢ 0 1 1 – – 15¢ – – 15¢ 1
0¢
Reset
5¢
N
N
N
10¢
D
15¢
[open]
D

## Slide 81: Example: Vending Machine (cont’d)
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 0 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 0 1 0 1 1 0 1 1 – – – 1 1 – – 1 1 1
Uniquely Encode States
0¢
5¢
10¢
15¢

## Slide 82: Example: Vending Machine (cont’d)
Mapping to Logic
D1 = Q1 + D + Q0 N
D0 = Q0’ N + Q0 N’ + Q1 N + Q1 D
OPEN = Q1 Q0
0 0 1 1
0 1 1 1
X X X X
1 1 1 1
Q1
D1
Q0
N
D
0 1 1 0
1 0 1 1
X X X X
0 1 1 1
Q1
D0
Q0
N
D
0 0 1 0
0 0 1 0
X X X X
0 0 1 0
Q1
Open
Q0
N
D
13 gates + 3 F/Fs
8 gates + 2 F/Fs

## Slide 83: Finite State Machine Optimization
State Minimization
  Fewer states require fewer state bits
  Fewer bits require fewer logic equations
Encodings: State, Inputs, Outputs
  State encoding with fewer bits has fewer equations to implement
    However, each may be more complex
  State encoding with more bits (e.g., one-hot) has simpler equations
    Complexity directly related to complexity of state diagram
  Input/output encoding may or may not be under designer control

## Slide 84: State Minimization Example
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
Sequence Detector for 010 or 110
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0

## Slide 85: Algorithmic Approach to State Minimization
Goal – identify and combine states that have equivalent behavior
Equivalent States:
  Same output
  For all input combinations, states transition to same or equivalent states
Row Matching Method: Algorithm Sketch
  1. Place all states in one set
  2. Initially partition set based on output behavior
  3. Successively partition resulting subsets based on next state transitions
  4. Repeat (3) until no further partitioning is required
    states left in the same set are equivalent
  Polynomial time procedure

## Slide 86: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 87: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 88: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 89: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 90: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 91: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
S1 is equivalent to S2
S3 is equivalent to S5
S4 is equivalent to S6
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 92: Minimized FSM
State minimized sequence detector for 010 or 110
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0
State
Minimization!

## Slide 93: Implication Chart Method
3-bit sequence detector example
  Take 3 bits as input. Output = 1 in case of 010 or 110

## Slide 94: Implication Chart Method: 3-bit seq. detector

## Slide 95: Implication Chart Method: 3-bit seq. detector
Check each equivalence candidate from top to down and left to right
For each candidate, check to see if each state transition is allowed
If not allowed, the candidate is not crossed out

## Slide 96: Implication Chart Method: 3-bit seq. detector
Check each equivalence candidate from top to down and left to right
For each candidate, check to see if each state transition is allowed
If not allowed, the candidate is not crossed out

## Slide 97: Implication Chart Method: 3-bit seq. detector
Check each equivalence candidate from top to down and left to right
For each candidate, check to see if each state transition is allowed
If not allowed, the candidate is not crossed out

## Slide 98: Implication Chart Method: 3-bit seq. detector
Check each equivalence candidate from top to down and left to right
For each candidate, check to see if each state transition is allowed
If not allowed, the candidate is not crossed out

## Slide 99: Results
S3=S5, S4=S6, S1=S2

## Slide 100: Sequence Detector Example
Design a sequence detector which takes as input 3 bits from an input bit stream and gives an output of ‘1’ when one of the patterns 111 and 010 is detected.
Given the following state transition diagram:
0/1
0/0
S0
Reset
1/0
S1
S2
S5
S3
S4
S6
0/0
1/0
0/0
0/0
0/0
1/0
1/0
1/0
1/1
1/0
0/0

## Slide 101: Sequence Detector Example
1. Reducing the number of states
  State Transition Table
Input Sequence | Present State | Next State |  | Output | 
 |  | X=0 | X=1 | X=0 | X=1
Reset | S0 | S1 | S2 | 0 | 0
0 | S1 | S3 | S4 | 0 | 0
1 | S2 | S5 | S6 | 0 | 0
00 | S3 | S0 | S0 | 0 | 0
01 | S4 | S0 | S0 | 1 | 0
10 | S5 | S0 | S0 | 0 | 0
11 | S6 | S0 | S0 | 0 | 1

## Slide 102: Sequence Detector Example
1. Reducing the number of states
  Implication Chart
S1 | S1-S3 S2-S4 |  |  |  |  | 
S2 | S1-S5 S2-S6 | S3-S5 S4-S6 |  |  |  | 
S3 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 |  |  | 
S4 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 | S0-S0 S0-S0 |  | 
S5 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 | S0-S0 S0-S0 | S0-S0 S0-S0 | 
S6 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 | S0-S0 S0-S0 | S0-S0 S0-S0 | S0-S0 S0-S0
 | S0 | S1 | S2 | S3 | S4 | S5
Input Sequence | Present State | Next State |  | Output | 
 |  | X=0 | X=1 | X=0 | X=1
Reset | S0 | S1 | S2 | 0 | 0
0 | S1 | S3 | S4 | 0 | 0
1 | S2 | S5 | S6 | 0 | 0
00 | S3 | S0 | S0 | 0 | 0
01 | S4 | S0 | S0 | 1 | 0
10 | S5 | S0 | S0 | 0 | 0
11 | S6 | S0 | S0 | 0 | 1

## Slide 103: Sequence Detector Example
1. Reducing the number of states
  Implication Chart
    Only S4 and S6 have output 1
S1 | S1-S3 S2-S4 |  |  |  |  | 
S2 | S1-S5 S2-S6 | S3-S5 S4-S6 |  |  |  | 
S3 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 |  |  | 
S4 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 | S0-S0 S0-S0 |  | 
S5 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 | S0-S0 S0-S0 | S0-S0 S0-S0 | 
S6 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 | S0-S0 S0-S0 | S0-S0 S0-S0 | S0-S0 S0-S0
 | S0 | S1 | S2 | S3 | S4 | S5
Present State | Next State |  | Output | 
 | X=0 | X=1 | X=0 | X=1
S4 | S0 | S0 | 1 | 0
S6 | S0 | S0 | 0 | 1

## Slide 104: Sequence Detector Example
1. Reducing the number of states
  Implication Chart
S1 | S1-S3 S2-S4 |  |  |  |  | 
S2 | S1-S5 S2-S6 | S3-S5 S4-S6 |  |  |  | 
S3 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 |  |  | 
S4 |  |  |  |  |  | 
S5 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 | S0-S0 S0-S0 |  | 
S6 |  |  |  |  |  | 
 | S0 | S1 | S2 | S3 | S4 | S5

## Slide 105: Sequence Detector Example
1. Reducing the number of states
  Implication Chart
S1 | S1-S3 S2-S4 |  |  |  |  | 
S2 | S1-S5 S2-S6 | S3-S5 S4-S6 |  |  |  | 
S3 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 |  |  | 
S4 |  |  |  |  |  | 
S5 | S1-S0 S2-S0 | S3-S0 S4-S0 | S5-S0 S6-S0 | S0-S0 S0-S0 |  | 
S6 |  |  |  |  |  | 
 | S0 | S1 | S2 | S3 | S4 | S5

## Slide 106: Sequence Detector Example
1. Reducing the number of states
  Implication Chart
S1 |  |  |  |  |  | 
S2 |  |  |  |  |  | 
S3 | S1-S0 S2-S0 |  |  |  |  | 
S4 |  |  |  |  |  | 
S5 | S1-S0 S2-S0 |  |  | S0-S0 S0-S0 |  | 
S6 |  |  |  |  |  | 
 | S0 | S1 | S2 | S3 | S4 | S5

## Slide 107: Sequence Detector Example
1. Reducing the number of states
  Implication Chart
S1 |  |  |  |  |  | 
S2 |  |  |  |  |  | 
S3 |  |  |  |  |  | 
S4 |  |  |  |  |  | 
S5 |  |  |  | S0-S0 S0-S0 |  | 
S6 |  |  |  |  |  | 
 | S0 | S1 | S2 | S3 | S4 | S5
S3=S5

## Slide 108: Sequence Detector Example
1. Reducing the number of states
  Reduced State Diagram
    S3 = S5
0/0
1/0
0/0
S0
Reset
1/0
S1
S2
S3
S5
S4
S6
0/0
0/1
0/0
0/0
1/0
1/0
1/1
1/0

## Slide 109: Sequence Detector Example
2. Encoding State Transition Table using reduced states
  State Transition Table(using reduced states)
Input Sequence | Present State | Next State |  | Output | 
 |  | X=0 | X=1 | X=0 | X=1
Reset | 000 | 001 | 010 | 0 | 0
0 | 001 | 011 | 100 | 0 | 0
1 | 010 | 011 | 110 | 0 | 0
00 or 10 | 011 | 000 | 000 | 0 | 0
01 | 100 | 000 | 000 | 1 | 0
11 | 110 | 000 | 000 | 0 | 1
Input Sequence | Present State | Next State |  | Output | 
 |  | X=0 | X=1 | X=0 | X=1
Reset | S0 | S1 | S2 | 0 | 0
0 | S1 | S3 | S4 | 0 | 0
1 | S2 | S5 | S6 | 0 | 0
00 | S3 | S0 | S0 | 0 | 0
01 | S4 | S0 | S0 | 1 | 0
10 | S5 | S0 | S0 | 0 | 0
11 | S6 | S0 | S0 | 0 | 1
Merge
Re-name

## Slide 110: Sequence Detector Example
2. Encoding State Transition Table using reduced states
  Truth Table(using reduced states)
Present State |  |  | X | Next State |  |  | OUTPUT
P2 | P1 | P0 |  | N2 | N1 | N0 | 
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1
1 | X | 1 | X | X | X | X | X

## Slide 111: Sequence Detector Example
3. Drawing K-maps and Obtaining 2-level SoP forms
P2P1 P0X | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 0
01 | 0 | 1 | 0 | 0
11 | 1 | 0 | X | X
10 | 0 | 0 | X | X
N2
P2P1 P0X | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 0
01 | 1 | 1 | 0 | 0
11 | 0 | 0 | X | X
10 | 1 | 0 | X | X
N1
P2P1 P0X | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 0
01 | 0 | 0 | 0 | 0
11 | 0 | 0 | X | X
10 | 1 | 0 | X | X
N0
P2P1 P0X | 00 | 01 | 11 | 10
00 | 0 | 0 | 0 | 1
01 | 0 | 0 | 1 | 0
11 | 0 | 0 | X | X
10 | 0 | 0 | X | X
OUTPUT
N2 = P2’P1P0X + P1’P0X
N1 = P2’P1P0’ + P2’P0’X + P1’P0X’
N0 = P2’P0’X’ + (P2’P1’X’ OR P1’P0X’)
OUTPUT = P2P1’X’ + P2P1X

## Slide 112: Sequence Detector Example
4. Drawing circuit schematics, with NAND, INV and D F/F
N2 = P2’P1P0’X + P1’P0X
N1 = P2’P1P0’ + P2’P0’X + P1’P0X’
Current state = D F/F outputs
Next state = D F/F inputs

## Slide 113: Sequence Detector Example
4. Drawing circuit schematics, with NAND, INV and D F/F
N0 = P2’P0’X’ + (P2’P1’X’ OR P1’P0X’)
OUTPUT = P2P1’X’ + P2P1X
Current state = D F/F outputs
Next state = D F/F inputs

## Slide 114: More Complex State Minimization
symbolic state transition table
present next state output state 00 01 10 11 S0 S0 S1 S2 S3 1 S1 S0 S3 S1 S4 0 S2 S1 S3 S2 S4 1 S3 S1 S0 S4 S5 0 S4 S0 S1 S2 S5 1 S5 S1 S4 S0 S5 0
inputs here
Multiple input example
10
01
11
00
00
01
11
10
10
01
11
00
10
00
11
00
11
10
01
10
11
01
00
S0 [1]
S2 [1]
S4 [1]
S1
[0]
S3
[0]
S5
[0]
01

## Slide 115: Minimized FSM
S0-S1
S1-S3
S2-S2
S3-S4
S0-S0
S1-S1
S2-S2
S3-S5
S0-S1
S3-S0
S1-S4
S4-S5
S0-S1
S3-S4
S1-S0
S4-S5
S1-S0
S3-S1
S2-S2
S4-S5
S4-S0
S5-S5
S1-S1
S0-S4
minimized state table
(S0==S4) (S3==S5)
present next state output state 00 01 10 11 S0' S0' S1 S2 S3' 1 S1 S0' S3' S1 S3' 0 S2 S1 S3' S2 S0' 1 S3' S1 S0' S0' S3' 0
Implication Chart Method
  Cross out incompatible states based on outputs
  Then cross out more cells if indexed chart entries are already crossed out
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4

## Slide 116: Overview
D F/F, register, and counter
Finite state machine design
State minimization
Design examples

## Slide 117
Case studies in Sequential Logic Design
Finite String Recognizer
A finite string recognizer has one input (X) and one output (Z).
The output is asserted whenever the input sequence …010…
has been observed, as long as the sequence …100… has not been
Seen since the last reset.
Step 1. Understanding the problem statement
Sample input/output behavior:
X: 00101010010…
Z: 00010101000…
X: 11011010010…
Z: 00000001000…

## Slide 118
Step 2. Draw State Diagrams for the strings that must be
recognized. I.e., 010 and 100.
Moore State Diagram
Reset signal places
FSM in S0
Outputs 1
Loops in State
Case studies in Sequential Logic Design
Finite String Recognizer

## Slide 119
Exit conditions from state S3:
if next input is 0 then have …0100 (state S6)
if next input is 1 then have …0101 (state S2)
Case studies in Sequential Logic Design
Finite String Recognizer

## Slide 120
Exit conditions from S1: recognizes strings of form …0 (no 1 seen)
loop back to S1 if input is 0
Exit conditions from S4: recognizes strings of form …1 (no 0 seen)
loop back to S4 if input is 1
Case studies in Sequential Logic Design
Finite String Recognizer

## Slide 121
S2, S5 with incomplete transitions
S2 = …01; If next input is 1, then string could be prefix of (01)1(00)
S4 handles just this case!
S5 = …10; If next input is 1, then string could be prefix of (10)1(0)
S2 handles just this case!
Final State Diagram
Case studies in Sequential Logic Design
Finite String Recognizer

## Slide 122
1. Write sample inputs and outputs to understand specification
2. Write sequences of states and transitions for the strings
to be recognized
3. Add missing transitions; reuse states as much as possible
4. Verify I/O behavior of your state diagram to insure it functions
like the specification
Review of Process:
Case studies in Sequential Logic Design
Finite String Recognizer
X: 00101010010…
Z: 00010101000…
X: 11011010010…
Z: 00000001000…

## Slide 123
Case studies in Sequential Logic Design
Finite String Recognizer
NS0 = CS2’·X
+ CS1·CS2·X’ + CS0·X’
NS1 = CS2·X + CS1·X’
+ CS0·CS2 + CS0·CS1
NS2 = CS0’·CS1’·X’
+ CS0’·CS2’·X’
+ CS1’·CS2’·X’
Z = CS0’·CS1·CS2
… too complex!
Implementation:

## Slide 124
Case studies in Sequential Logic Design
Finite String Recognizer
Implementation: Another approach
Let’s use shift register!
With shift register, we can now design a different state machine
using P010 and P100 as inputs
S1
[1]
S0
[0]
S2
[0]
Reset
P100
P100
P010

## Slide 125
Case studies in Sequential Logic Design
Finite String Recognizer
Implementation: Another approach
NS0 = CS0 + P100
NS1 = CS0’·P010
Z = CS1

## Slide 126
Case studies in Sequential Logic Design
Complex Counter
A sync. 3 bit counter has a mode control M. When M = 0, the counter
counts up in the binary sequence. When M = 1, the counter advances
through the Gray code sequence.
Binary: 000, 001, 010, 011, 100, 101, 110, 111, …
Gray: 000, 001, 011, 010, 110, 111, 101, 100, …
One state for each output combination
Add appropriate arcs for the mode control

## Slide 127
Case studies in Sequential Logic Design
Complex Counter
Mode Input (M)
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
Current State
000
000
001
001
010
010
011
011
100
100
101
101
110
110
111
111
Next State (Z2 Z1 Z0)
001
001
010
011
011
110
100
010
101
000
110
100
111
111
000
101

## Slide 128
Case studies in Sequential Logic Design
Complex Counter
We’ll implement this Complex Counter using 4-bit sync. counter
To move next Gray-code state, we’ll load these values into counter
when M is asserted.
4-bit sync. counter
Current State
P2 P1 P0
000
001
010
011
100
101
110
111
Next State(Gray)
G2 G1 G0
001
011
110
010
000
100
111
101
EN
UP D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
G2 = P2·P0 + P1·P0’
G1 = P2’·P0 + P1·P0’
G0 = P2’·P1’ + P2·P1
Counter operates on binary mode when
Up is HIGH
EN is HIGH
Counter loads new inputs
when LOAD is HIGH

## Slide 129
Case studies in Sequential Logic Design
Complex Counter
G2 = P2·P0 + P1·P0’
G1 = P2’·P0 + P1·P0’
G0 = P2’·P1’ + P2·P1
Counter operates on binary mode when
Up is HIGH(connected to M’)
EN is HIGH(connected to M’)
Counter loads new inputs(operates on Gray mode)
when LOAD is HIGH(connected to M)
Complete schematic

## Slide 130
Case studies in Sequential Logic Design
Digital Combination Lock
“A 3-digit serial lock controls entry to locked room.
Inputs are RESET, ENTER, and a 16-key keypad, on which the user
can enter one value at a time.
Locks generates an UNLOCK signal when key matches combination.
ERROR light illuminated if key does not match combination.”
To open the door:
Press RESET, (2) enter key for first digit, (3) Press ENTER,
(4) Repeat (2),(3) for second/third digits
E.g., if you type in 208, Press RESET -> Press ‘2’ -> Press ENTER
-> Press ‘0’ -> Press ENTER -> Press ‘8’ -> Press ENTER
If all three key were correct, the door will be opened.
Internal
Combination
Operator Data
Inputs:
RESET
ENTER
VALUE (4bit)
(LD1, LD2, LD3)
Outputs:
Unlock
Error
UNLOCK
ERROR
RESET
ENTER
VALUE
Combination
Lock FSM
4
C2
C3
C1
clk
LD1
LD2
LD3

## Slide 131
Case studies in Sequential Logic Design
Digital Combination Lock
C2==Value
& ENTER
S1
[MUXC1]
Reset
C1!=Value
& ENTER
S2
[MUXC2]
S3
[MUXC3]
OPEN
[UNLOCK]
ERROR
C2!=Value
& ENTER
C3!=Value
& ENTER
C1==Value
& ENTER
C3==Value
& ENTER
ENTER’
ENTER’
ENTER’
State diagram for the combination lock

## Slide 132
Case studies in Sequential Logic Design
Digital Combination Lock
Block diagram for the combination lock
Multiplexer
Controller
Comparator
C1
C2
C3
4
4
4
4
4
VALUE
MUX control
Equal
ENTER
RESET
Unlock
CLK
Datapath
Controller

## Slide 133
Case studies in Sequential Logic Design
Digital Combination Lock
Multiplexer
Controller
Comparator
C1
C2
C3
4
4
4
4
4
VALUE
MUX control
Equal
ENTER
RESET
Unlock
CLK
Block diagram for the combination lock
2
0
8

## Slide 134
Case studies in Sequential Logic Design
Digital Combination Lock
Controller

## Slide 135
Case studies in Sequential Logic Design
Digital Combination Lock
Datapath

## Slide 136
Case studies in Sequential Logic Design
Digital Combination Lock
Top module

## Slide 137
Design of a Simple Memory Controller
Generation of control signals from overlapping clocks, f1, f2, f3 and f4
Case studies in Sequential Logic Design
Memory controller

## Slide 138
Design of a Simple Memory Controller
Multi-phase clock for sequencer
Case studies in Sequential Logic Design
Memory controller
D
Q
D
Q
D
Q
D
Q
IN
f1
f2
f3
f4
CLK
f1
f2
f3
f4
IN
Time
C = f1f2f3’f4’+f1’f2’f3’f4

## Slide 139
Design of a Simple Memory Controller
Generation of control signals from overlapping clocks, f1, f2, f3 and f4
Case studies in Sequential Logic Design
Memory controller
F1 F2 R/W

## Slide 140: Making connections
multiplexer
demultiplexer
4x4 switch
control
control
Direct point-to-point connections between gates
  wires we've seen so far
Route one of many inputs to a single output - multiplexer (MUX)
Route a single input to one of many outputs - demultiplexer (DEMUX)
Two popular regular logic components are MUX and DEMUX. A MUX selects one of its data inputs to the output by the control inputs; a MUX is also called a selector. The diagram on the left shows a 4-input MUX. Can you guess the relation between the number of data inputs and the number of control lines? A DEMUX performs the reverse function, often called a decoder. We can clearly see that these components perform higher-level functions compared to logic gates

## Slide 141
A hardware to communicate over a single wire (using RS-232 serial line protocol)
The data will be sent serially, and the circuit works in general case when the clocks on the two ends are completely asynchronous.
The hardware consists of two circuits.
  The first circuit will take input from a telephone-like keypad and send a byte corresponding to the key that was pressed over a single wire one bit at a time.
  The second circuit will receive the serial data sent by the first and display it on a small LCD screen.
RS-232 serial line protocol for one byte of data
Quiescent value (normally high)
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver

## Slide 142
Oversampling
It may miss the start bit between two high values if it samples the wire once every bit time.
It needs a faster clock that will sample the wire faster than once every bit cycle (in this case, 4 times during each bit time)
Block diagram of serial line transmitter/receiver
Implementation
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver

## Slide 143
Block diagram of serial line transmitter/receiver(Cont’d)
Sender part
Receiver part
KeyboardDecode: Decoding the signals from the keypad and turn them in to the appropriate character code for the button that was pressed
Sender: Taking the byte and serially transmits it over the single wire
Receiver: Observing the signal wire coming from the sender and determines when a byte has been received
DisplayControl: Taking the data and controls the LCD appropriately to get the corresponding character to show up on the screen
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver

## Slide 144
Schematic diagram of a keyboard block with debouncing circuitry
Keyboard
Schematic diagram of a single keyboard key
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver

## Slide 145
KeyboardDecode
module KeyboardDecode (ClkS, ResetS, R1, R2, R3, R4, C1,
C2, C3, AckS, Send, CharToSend);
input ClkS, ResetS, R1, R2, R3, R4, C1, C2, C3, AckS;
output Send;
output [7:0] CharToSend;
reg [7:0] CharToSend;
reg Send;
wire KeyPress;
assign KeyPress = (R1 || R2 || R3 || R4) && (C1 || C2 || C3);
always @(posedge ClkS) begin
if (ResetS) begin Send <=0; end
else begin
if (KeyPress && !AckS) begin
if (R1 && C1) CharToSend <= 8'b00110001;
//code for 1
else if (R1 && C2) CharToSend <= 8'b00110010;
//code for 2
else if (R1 && C3) CharToSend <= 8'b00110011;
//code for 3
else if (R2 && C1) CharToSend <= 8'b00110100;
//code for 4
else if (R2 && C2) CharToSend <= 8'b00110101;
//code for 5
else if (R2 && C3) CharToSend <= 8'b00110110;
//code for 6
else if (R3 && C1) CharToSend <= 8'b00110111;
//code for 7
else if (R3 && C2) CharToSend <= 8'b00111000;
//code for 8
else if (R3 && C3) CharToSend <= 8'b00111001;
//code for 9
else if (R4 && C1) CharToSend <= 8'b00101010;
//code for *
else if (R4 && C2) CharToSend <= 8'b00110000;
//code for 0
else if (R4 && C3) CharToSend <= 8'b00100011;
//code for #
Send <=1;
end
if (AckS) Send <=0;
end
end
endmodule
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver
Key
pressed
AckS=1
Send=1
Send=0

## Slide 146
Sender
module Sender (ClkS, ResetS, Send, CharToSend, AckS, TxD);
input ClkS, ResetS, Send;
input [7:0] CharToSend;
output AckS, TxD;
reg TxD; // register alias for RS232 line
reg [7:0] charToSend; // holds character to be sent over
// the serial line
reg [3:0] bitCounter; // keeps count of which bit is
// being sent
reg go;
always @(posedge ClkS) begin
if (ResetS) begin TxD <= 1; go <= 0; end
else begin
if (Send) begin
// load character sent from keypad and hold
// it just in case
// reset bitCounter to zero for start of new
// transmission and set the go bit
charToSend <= CharToSend;
bitCounter <= 0; go <= 1;
end
else begin
bitCounter <= bitCounter + 1;
// if go is set, it's time to send the
// next bit of the 10 to be sent -
// start bit, 8 bits of character to send
// (most significant bit first),
// and a stop bit at the end - reset go when done
if (go) begin
if (bitCounter == 0) TxD <= 0;
else if (bitCounter > 0 && bitCounter <= 8)
TxD <= charToSend[8 - bitCounter];
else if (bitCounter > 8) begin
TxD <= 1;
go <= 0;
end
end
end
end
end
assign AckS = go;
endmodule
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver
ClkS
ResetS
Key
pressed
AckS=1
Send=1
Send=0

## Slide 147
Sender
module Sender (ClkS, ResetS, Send, CharToSend, AckS, TxD);
input ClkS, ResetS, Send;
input [7:0] CharToSend;
output AckS, TxD;
reg TxD; // register alias for RS232 line
reg [7:0] charToSend; // holds character to be sent over
// the serial line
reg [3:0] bitCounter; // keeps count of which bit is
// being sent
reg go;
always @(posedge ClkS) begin
if (ResetS) begin TxD <= 1; go <= 0; end
else begin
if (Send) begin
// load character sent from keypad and hold
// it just in case
// reset bitCounter to zero for start of new
// transmission and set the go bit
charToSend <= CharToSend;
bitCounter <= 0; go <= 1;
end
else begin
bitCounter <= bitCounter + 1;
// if go is set, it's time to send the
// next bit of the 10 to be sent -
// start bit, 8 bits of character to send
// (most significant bit first),
// and a stop bit at the end - reset go when done
if (go) begin
if (bitCounter == 0) TxD <= 0;
else if (bitCounter > 0 && bitCounter <= 8)
TxD <= charToSend[8 - bitCounter];
else if (bitCounter > 8) begin
TxD <= 1;
go <= 0;
end
end
end
end
end
assign AckS = go;
endmodule
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver
Key
pressed
AckS=1
Send=1
Send=0
D7
D6 ….
TxD=0

## Slide 148
Block diagram of serial line transmitter/receiver(Cont’d)
Sender part
Receiver part
KeyboardDecode: Decoding the signals from the keypad and turn them in to the appropriate character code for the button that was pressed
Sender: Taking the byte and serially transmits it over the single wire
Receiver: Observing the signal wire coming from the sender and determines when a byte has been received
DisplayControl: Taking the data and controls the LCD appropriately to get the corresponding character to show up on the screen
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver

## Slide 149
Receiver
module Receiver (ClkR, ResetR, RxD, AckR, CharRcvd, Rcvd);
input ClkR, ResetR, RxD, AckR;
output [7:0] CharRcvd;
output Rcvd;
reg [4:0] bitCounter; // keep count of number of bits received
reg [1:0] cycleCounter; // used to divide input clock by 4
reg [8:0] characterReceived; // start bit plus 8 data bits
reg go; // flag indicating a character is arriving
// finite state machine to receive characters
always @(posedge ClkR) begin
if (ResetR) begin go <= 0; Rcvd <= 0; end
else begin
if (!go && !Rcvd && !AckR && RxD) ;
//serial line is still quiet, nothing to do
if (!go && !Rcvd && !AckR && !RxD) begin
//found a start bit, reset the counters
go <=1; bitCounter <= 0; cycleCounter <= 0;
end
if (go) begin // every four cycles . . .
if (cycleCounter == 0) begin
// copy sample into character bit array
characterReceived[8 - bitCounter] <= RxD;
// if the counter has not reached 8,
// increment it
if (bitCounter < 8)
bitCounter <= bitCounter + 1;
else begin
// otherwise, signal that the entire character has been received by
// starting handshake and resetting
// counter and flag
go <= 0;
Rcvd <= 1;
end
end
cycleCounter <= cycleCounter + 1;
// increment counter
end
if (AckR) Rcvd <= 0;
// complete four cycle
// handshake with DisplayControl
end
end
// connect the CharRcvd lines to the character received
// ignoring the start bit
assign CharRcvd[7:0] = characterReceived[7:0];
endmodule
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver
1
RxD
0
1
2
3
0
Rcvd=1
cycleCounter

## Slide 150
Display
Operation | RS | DB7 . . . DB0
Clear display | 0 | 0000 0001
Function set | 0 | 0011 0011
Display on | 0 | 0000 1100
Entry mode set | 0 | 0000 0110
Write character | 1 | DDDD DDDD
Timing of LCD screen interface
LCD screen operations
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver

## Slide 151
DisplayControl
module DisplayControl (ClkR, ResetR, Rcvd, CharRcvd,
AckR, DB, RS, Enable);
input ClkR, ResetR, Rcvd;
input [7:0] CharRcvd;
output AckR, RS, Enable;
output [7:0] DB;
reg [7:0] databus; // internal databus that can
// be connected to DB lines
reg Enable; // register aliasing for
// LCD screen E signal
reg RS; // register aliasing for
//screen RS signal
reg AckR; // signal to Rcvr module to
// clear its Rcvd output
// this implements a four-cycle
// handshake with Rcvd
reg initMode; // indicates whether the initialize
// sequence is in progress
reg [4:0] initState; // states for initialization sequence
parameter start = 0;
parameter step1 = 1;
parameter endstep1 = 2;
parameter step2 = 3;
parameter endstep2 = 4;
parameter step3 = 5;
parameter endstep3 = 6;
parameter step4 = 7;
parameter endstep4 = 8;
parameter final = 9;
// drive DB lines from internal databus during
// initialization sequence
// or from CharRcvd register when displaying characters
assign DB = (initMode) ? databus : CharRcvd;
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver

## Slide 152
DisplayControl(Cont’d)
always @(posedge ClkR) begin
if (ResetR) begin initMode <= 1; initState <= start;
Enable <= 0; AckR <= 0; end
else if (initMode) begin
// do initialization sequence
case (initState)
start: // set display to receive commands
begin RS <= 0; initState <= step1; end
step1: // 1st step of initialization
// sequence - clear display
begin Enable <= 1; databus <= 8'b00000001;
initState <= endstep1; end
endstep1:
begin Enable <= 0; initState <= step2; end
step2: // 2nd step of initialization sequence -
// function set
begin Enable <= 1; databus <= 8'b00110011;
initState <= endstep2; end
endstep2:
begin Enable <= 0; initState <= step3; end
step3: // 3rd step of initialization sequence -
// display on
begin Enable <= 1; databus <= 8'b00001100;
initState <= endstep3; end
endstep3:
begin Enable <= 0; initState <= step4; end
step4: // 4th step of initialization sequence -
// entry mode set
begin Enable <= 1; databus <= 8'b00000110;
initState <= endstep4; end
endstep4:
begin Enable <= 0; initState <= final; end
final:
begin
RS <= 1; // Set display to
// receive characters
initMode <= 0; // indicate initialize
// completed
initState <= final; // stay in this state
// until next reset
end
endcase
end
else begin
// or see if character has been received
if (Rcvd && !AckR) begin
// character has been received by Receiver module
// display character on display
// begin handshake with Receiver module by
// raising AckR
case (Enable)
0: begin Enable <= 1; end
1: begin Enable <= 0; AckR <= 1; end
endcase
end
else begin
// complete handshake with Receiver module by
// lowering AckR
// after Rcvd is lowered
if (!Rcvd) AckR <= 0;
end
end
end
endmodule
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver
(1)
(2)
(3)
(1)
(2)
(3)
Rcvd
Rcvd
AckR
AckR
CharRcvd
CharRcvd
Receiver
DisplayCtrl

## Slide 153
Block diagram of serial line transmitter/receiver(Cont’d)
Sender part
Receiver part
KeyboardDecode: Decoding the signals from the keypad and turn them in to the appropriate character code for the button that was pressed
Sender: Taking the byte and serially transmits it over the single wire
Receiver: Observing the signal wire coming from the sender and determines when a byte has been received
DisplayControl: Taking the data and controls the LCD appropriately to get the corresponding character to show up on the screen
Case studies in Sequential Logic Design
A Serial Line Transmitter/Receiver

## Slide 154: Thank You! Q&A