## Slide 1: Chapter 6. Sequential logic design
This is the beginning of the second part of this course, sequential logic.

## Slide 2: Sequential logic
Sequential circuits
  Simple circuits with feedback
  Latches
  Edge-triggered flip-flops
Basic registers
  Register file
  Shift registers
  Simple counters
Asynchronous input
  Metastability problem
  Double F/Fs
Again, sequential logic circuits are quite different from combinational logic. In general, sequential systems are more difficult to design. We will discuss some basic issues in the sequential logic systems in this chapter including how to handle asynchronous input.

## Slide 3: Simplest circuits with feedback
"remember"
"load"
"data"
"stored value"
Let’s consider a simple memory element first. What if we place two inverters before a stored value and suppose the stored value is 1. Note that there is a feedback from the stored value to the first inverter. Another more sophisticated option is to have a selection function between a stored value and a new value. If “load” is enabled, the new “data” will be put into the stored value.
Two inverters form a static memory cell
  will hold value as long as it has power applied
How to get a new value into the memory cell?
  selectively break feedback path
  load new value into cell
"0"
"1"
"stored value"

## Slide 4: Memory with cross-coupled gates
R
S
Q
Q'
R
S
Q
R'
S'
Q
Q
Q'
S'
R'
Let’s consider this feedback in the cases of cross-connectivity between other gate types. With Nor or Nand gates, we can have more control inputs. R and S denote reset and set inputs, respectively. Q is the output value of interest and its inverse is denoted by Q’. For a NOR gate, think of a case when a single input can determine the output of the gate. Suppose R is 1, which makes Q 0. Basically, we assume R and S are opposite for update.
Q'
Cross-coupled NOR gates (R-S Latch)
  similar to inverter pair, with capability to force output to 0 (reset=1) or 1 (set=1)
Cross-coupled NAND gates
  similar to inverter pair, with capability to force output to 0 (R’=0) or 1 (S’=0)
Q'

## Slide 5: R-S latch analysis
5
Q(t+)
R
S
Q(t)
S R Q(t) Q(t+) 0 0 0 0 0 0 1 1 0 1 0 0 0 1 1 0 1 0 0 1 1 0 1 1 1 1 0 X 1 1 1 X
hold
reset
set
not allowed
characteristic equation
Q(t+) = S + R’ Q(t)
Break feedback path
R
S
Q
Q'
0 0
1 0
X 1
X 1
Q(t)
R
S
To analyze the timing, let’s assume the feedback loop is cut off. That is, consider Q(t) and Q(t+ ∆) separately. Here ∆ is the delay incurred by the latch. When you look at the truth table, you can notice something different. What is it?

## Slide 6: Timing behavior
The problem happens when R=S=1. Are Q and Q’ just 0s? The more significant problem arises when R=S=1 and then R=S=0, which will yield an oscillation as follows. Q and Q’ will be 1 together. But then Q and Q’ should be changed to 0 again. Then this cycle continues.
Reset
Hold
Set
Set
Reset
Race
R
S
Q
\Q
100
R
S
Q
Q'
If R=1 and S=0, Q is 0 and Q’ is 1 (recall the meaning of reset R). If R=0 and S=1, Q is 1. What if R=S=0, then Q and Q’ will remain with the previous values.

## Slide 7: Gated R-S latch
The next version is a gated R-S latch. In the gated (level-sensitive) R-S latch, the R-S values are handled cautiously. When enable’ is high, then R and S are always zeroes (there is no glitch or fluctuation in R and S). So R’ and S’ are meaningful only when enable’ is low. This waveform shows when enable is high and S is set (or S’ is low), Q will become true.
enable’
S'
Q'
Q
R'
R
S
Enable controls when R and S inputs matter
  otherwise, the slightest glitch on R or S could cause change in value stored
Set
Reset
S'
R'
enable’
Q
Q'
100

## Slide 8: Clocks
period
duty cycle (in this case, 50%)
Used to keep time
  wait long enough for inputs (R' and S') to settle
  then allow to have effect on value stored
Clocks are regular periodic signals
  period (time between ticks)
  duty-cycle (time clock is high between ticks - expressed as % of period)
A clock is an important element in sequential circuits. The enable signal in the previous slide serves as kind of a clock. Once enable is asserted, it should remain high until the input stimulates the output fully. Normally, a clock is periodically alternating between high and low. The beginning of each period is called a clock tick. And the duty cycle is defined as the ratio of High voltage interval to the period.

## Slide 9: Clocks (cont’d)
Controlling an R-S latch with a clock
  Change R and S while clock’ is 1 (inject new input)
    only have half of clock period for signal changes to propagate
  Keep R and S stable while clock’ is 0 (allowing R and S to pass)
    signals must be stable for the other half of clock period
clock’
S’
Q’
Q
R’
R
S
clock’
R’ and S’
changing
stable
changing
stable
stable
Let’s control the gated (or level-sensitive) R-S latch with a clock. While clock’ is 0, R’ and S’ should sustain their values which will update Q and Q’ during that interval. While clock’ is high, R’ and S’ can be changed to a new value (for next operation); in the meantime, Q and Q’ will not change since R and S are 00.

## Slide 10: Master-slave structure
Break flow by alternating clocks
  use positive clock to latch inputs into one R-S latch
  use negative clock to change outputs with another R-S latch
View pair as one basic unit
  master-slave flip-flop
  twice as much logic
  output changes a few gate delays after the falling edge of clock
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’
R
S

## Slide 11: The 1s catching problem
Set
1s catch
S
R
CLK
P
P’
Q
Q’
Reset
Master Outputs
Slave Outputs
In first R-S stage of master-slave FF
  0-1-0 glitch on R or S while clock is high is "caught" by master stage
  leads to constraints on logic to be hazard-free
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’
R
S
What would be the problem of the inverted clock signals for the pair of R-S latches? While the clock is high, suppose there is a glitch is in the very first S (0-1-0), P and P’ will change, which in turn will affect the slave latch when the clock becomes low. This is called the 1s catching problem.

## Slide 12: D flip-flop
To eliminate the 1s catching problem, we have to make S and R have opposite values; so we use the complementary values from the same input, which is called D flip-flop. D is an abbreviation for data. So R and S can be either 01 and 10 only. Now we cannot use 00 to maintain the same value in the latch. How many gates here? Each R-S latch has two NOR gates.
10 gates
Make S and R complements of each other
  eliminates 1s catching problem
  can't just hold previous value (must have new value ready every clock period)
  value of D just before clock goes low is what is stored in flip-flop
    negative edge-triggered
D
Q
Q’
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’

## Slide 13: (Negative) Edge-triggered D flip-flops (FFs)
The other realization to solve the 1s catching problem is to use a clock edge to trigger the change of the flip-flop’s value. While the clock is high, the second top NOR and the second bottom NOR gates will be 0, which keeps the old values of Q and Q’
Q
D
Clk=1
R
S
0
D’
0
D’
D
Q’
negative edge-triggered D flip-flop (D-FF)
4-5 gate delays
must respect setup and hold time constraints to successfully capture input
characteristic equation Q(t+1) = D
holds D’ when
clock goes low
holds D when clock goes low
More efficient solution: only 6 gates
  sensitive to inputs only near edge of clock signal (not while high)

## Slide 14: Negative Edge-triggered D flip-flops (cont’d)
If clock goes from 1 to 0, initially S and R are 0. Then, depending on D’s value, S or R will be changed, which in turn will set or reset Q. The numbers in blue show the case when D is 0. After that, D’s change makes no effect. E.g. new D is 1 now, D (second bottom NOR) was 0, D’(bottom) becomes 0. So D (top) is still 0; R and S are not changed.
Step-by-step analysis
Q
D
Clk=0
R
S
D
D’
D’
D’
D
when clock goes high-to-low data is latched
when clock is low, data is held
Q
new D
Clk=0
R
S
D
D’
D’
D’
D
new D = 1  old D
0
0
1
10
0
1
1
0
0
1
1
1
1
0
1
1
0

## Slide 15: Edge-triggered D flip-flops (cont’d)
positive edge-triggered FF
negative edge-triggered FF
D
CLK
Qpos
Qpos’
Qneg
Qneg’
100
Positive edge-triggered
  inputs sampled on rising edge; outputs change after rising edge
Negative edge-triggered flip-flops
  inputs sampled on falling edge; outputs change after falling edge
There are two kinds of flip-flops which are triggered by the two edges of the signals: rising edge and falling edge. The previous slide shows a negative edge-triggered FF. If we add an inverter to the clock, that FF is turned into a positive edge-triggered FF. Typically, latches are level triggered and simpler. FFs are mostly edge triggered and more complicated.

## Slide 16: Edge-triggered D flip-flops (cont’d)
positive edge-triggered FF
negative edge-triggered FF
D
CLK
Qpos
Qpos’
Qneg
Qneg’
100
Positive edge-triggered
  inputs sampled on rising edge; outputs change after rising edge
Negative edge-triggered flip-flops
  inputs sampled on falling edge; outputs change after falling edge
There are two kinds of flip-flops which are triggered by the two edges of the signals: rising edge and falling edge. The previous slide shows a negative edge-triggered FF. If we add an inverter to the clock, that FF is turned into a positive edge-triggered FF. Typically, latches are level triggered and simpler. FFs are mostly edge triggered and more complicated.
1
1
0

## Slide 17: D flip-flop
To eliminate the 1s catching problem, we have to make S and R have opposite values; so we use the complementary values from the same input, which is called D flip-flop. D is an abbreviation for data. So R and S can be either 01 and 10 only. Now we cannot use 00 to maintain the same value in the latch. How many gates here? Each R-S latch has two NOR gates.
10 gates
Make S and R complements of each other
  eliminates 1s catching problem
  can't just hold previous value (must have new value ready every clock period)
  value of D just before clock goes low is what is stored in flip-flop
    negative edge-triggered
D
Q
Q’
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’
1
1
1
0

## Slide 18: D flip-flop
To eliminate the 1s catching problem, we have to make S and R have opposite values; so we use the complementary values from the same input, which is called D flip-flop. D is an abbreviation for data. So R and S can be either 01 and 10 only. Now we cannot use 00 to maintain the same value in the latch. How many gates here? Each R-S latch has two NOR gates.
10 gates
Make S and R complements of each other
  eliminates 1s catching problem
  can't just hold previous value (must have new value ready every clock period)
  value of D just before clock goes low is what is stored in flip-flop
    negative edge-triggered
D
Q
Q’
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’
1
0
1
1
1

## Slide 19: Edge-triggered D flip-flops (cont’d)
positive edge-triggered FF
negative edge-triggered FF
D
CLK
Qpos
Qpos’
Qneg
Qneg’
100
Positive edge-triggered
  inputs sampled on rising edge; outputs change after rising edge
Negative edge-triggered flip-flops
  inputs sampled on falling edge; outputs change after falling edge
There are two kinds of flip-flops which are triggered by the two edges of the signals: rising edge and falling edge. The previous slide shows a negative edge-triggered FF. If we add an inverter to the clock, that FF is turned into a positive edge-triggered FF. Typically, latches are level triggered and simpler. FFs are mostly edge triggered and more complicated.
1
0
1

## Slide 20: Comparison of latches and flip-flops (FFs)
behavior is the same unless input changes
while the clock is high
D Q
CLK
positive edge-triggered flip-flop
D Q
C
CLK
transparent (level-sensitive) latch
D
CLK
Qedge
Qlatch
Again, in FFs, the data value only at the rising edge (or falling edge) is critical (see blue dots). Meanwhile, most latches are sensitive to D value changes as long as the clock is high. Typically, the clock input of a FF is depicted by a triangle.

## Slide 21: Timing Problem
If the input changes values at clock edge, the D F/F will give unknown value
Solution? Stable input at clock edge!
Thus, we have a timing constraint that the input needs to be stable at clock edge.
10 gates
What if input changes at clock edge?
  The first latch may not be able to keep the previous or new value
  We cannot tell what value the second latch catches
  Finally, the D F/F output will be unknown (X)
  How can we resolve this timing problem?
   Stable input at clock edge
D
Q
Q’
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’
10
10
1?
0?

## Slide 22: Timing constraints
Definition of terms
  clock: periodic event, causes state of memory element to change can be rising edge or falling edge or high level or low level
  setup time: minimum time before the clocking event by which the input must be stable (Tsu)
  hold time: minimum time after the clocking event until which the input must remain stable (Th)
Let’s go over terminologies first. We already know what is a clock. For each edge of a clock signal, there are some timing constraints. Suppose the positive edge of a clock signal triggers a circuit. Then the data input should be stable for an interval which is Tsu+Th, which are dependent on transistor circuit delay.
there is a timing "window" around
the clocking event during which the
input must remain stable and
unchanged in order to be recognized
clock
data
changing
stable
input
clock
Tsu
Th
clock
data
D
Q

## Slide 23: Typical timing specifications
This slide illustrates the timing where the rising edge of the clock signal is the reference. Tpd is the propagation delay between the rising edge of the clock (event trigger) and the change in the output. Tw should be long enough to ensure that D will change Q
all measurements are made from the clocking event (the rising edge of the clock)
Positive edge-triggered D flip-flop
  setup (Tsu) and hold (Th) times
  Tpd: propagation delays (low to high, high to low, max and typical)
  Clock period > Tsu + Tpd
D
Clk
Q
T
su
1.8
ns
T
h
0.5
ns
T
w
3.3
ns
T
pd
3.6 ns
1.1 ns
T
su
1.8
ns
T
h
0.5
ns
T
pd
3.6 ns
1.1 ns
T
w
3.3
ns

## Slide 24: Propagation Delay
Delay of 2nd latch
  After clock goes low, it takes time for the 2nd latch to give the new output
D
Q
Q’
master stage
slave stage
P
P’
CLK
R
S
Q
Q’
R
S
Q
Q’
1
10
1
01
Tpd

## Slide 25: Typical timing specifications
This slide illustrates the timing where the rising edge of the clock signal is the reference. Tpd is the propagation delay between the rising edge of the clock (event trigger) and the change in the output. Tw should be long enough to ensure that D will change Q
all measurements are made from the clocking event (the rising edge of the clock)
Positive edge-triggered D flip-flop
  setup (Tsu) and hold (Th) times
  Tpd: propagation delays (low to high, high to low, max and typical)
  Clock period > Tsu + Tpd
D
Clk
Q
T
su
1.8
ns
T
h
0.5
ns
T
w
3.3
ns
T
pd
3.6 ns
1.1 ns
T
su
1.8
ns
T
h
0.5
ns
T
pd
3.6 ns
1.1 ns
T
w
3.3
ns

## Slide 26: Cascading Edge-triggered Flip-Flops
IN
Q0
Q1
CLK
100
Shift register
  New value goes into first stage
  While previous value of first stage goes into second stage
  Consider setup/hold/propagation delays (Tpd must be > Th)
CLK
IN
Q0
Q1
D
Q
D
Q
OUT

## Slide 27: Cascading Edge-triggered Flip-Flops (cont’d)
timing constraints
guarantee proper
operation of
cascaded components
assumes infinitely fast distribution of the clock
Why this works
  Propagation delays exceed hold times
  Clock width constraint exceeds setup time
  This guarantees following stage will latch current value before it changes to new value
Tsu
4ns
Tp
3ns
Th
2ns
In
Q0
Q1
CLK
Tsu
4ns
Tp
3ns
Th
2ns
Q
D
Clk=1
R
S
0
D’
0
D’
D
Q’

## Slide 28: Timing Methodologies
clock
data1 & 2
changing
stable
F/F-controlled system (positive edge triggered)
clock
data1
D
Q
D
Q
data2
Positive edge-triggered
Setup time violation
Hold time violation

## Slide 29: Verilog Code #2: Sequential Logic
Flip-flops
Memory elements
Shift registers
Counters

## Slide 30: D-Type Flip-Flops
// D-type flip-flop
module DFF (clk, d, q);
input clk, d;
output reg q;
always @(posedge clk) q <= d;
endmodule
q

## Slide 31: Asynchronous Reset D-Type Flip-Flops
// asynchronous reset D-type flip-flop
module DFF_async_reset (clk, reset_n, d, q);
input clk, reset_n, d;
output reg q;
always @(posedge clk or negedge reset_n)
if (!reset_n) q <= 0;
else q <= d;
endmodule
q
reset_n
X
q
O

## Slide 32: Synchronous Reset D-Type Flip-Flops
// synchronous reset D-type flip-flop
module DFF_sync_reset (clk, reset_n, d, q);
input clk, reset_n, d;
output reg q;
always @(posedge clk)
if (!reset_n) q <= 0;
else q <= d;
endmodule
q
reset_n

## Slide 33: Sequential Logic
Flip-flops
Memory elements
Shift registers
Counters

## Slide 34: Registers
R
S
R
S
R
S
D
Q
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
OUT4
CLK
IN1
IN2
IN3
IN4
R
S
"0"
Collections of flip-flops with similar controls and logic
  stored values somehow related (for example, form binary value)
  share clock, reset, and set lines
  similar logic at each stage
Examples
  shift registers
  counters
From now on, we will look at a collection of FFs. The first memory element to look at is a register. A register is normally defined as a group of FFs with coordinated controls or shared controls. Examples of controls are clock, reset, set and so on. In this case, we can read/write 4 bits in parallel.

## Slide 35: Data Registers
// D-type flip-flop
module DFF (clk, din, qout);
input clk, din;
output reg qout;
always @(posedge clk) qout <= din;
endmodule

## Slide 36: Data Registers
// an n-bit data register
module register(clk, din, qout);
parameter N = 4; // number of bits
…
input [N-1:0] din;
output reg [N-1:0] qout;
always @(posedge clk) qout <= din;
endmodule

## Slide 37: Data Registers
// an N-bit data register with asynchronous reset
module register_reset (clk, reset_n, din, qout);
parameter N = 4; // number of bits
…
input [N-1:0] din;
output reg [N-1:0] qout;
always @(posedge clk or negedge reset_n)
if (!reset_n) qout <= {N{1'b0}};
else qout <= din;
endmodule

## Slide 38: Data Registers
// an N-bit data register with synchronous load and asynchronous reset
module register_load_reset (clk, load, reset_n, din, qout);
parameter N = 4; // number of bits
input clk, load, reset_n;
input [N-1:0] din;
output reg [N-1:0] qout;
always @(posedge clk or negedge reset_n)
if (!reset_n) qout <= {N{1'b0}};
else if (load) qout <= din;
endmodule

## Slide 39: Register File
A key component in CPU
A set of registers + Mux/DeMux
[Intel] [http://fourier.eng.hmc.edu/e85_old/lectures/figures/register_file_diagram_0.gif]

## Slide 40: A Register File (having 16 8-bit Words)
// an N-word register file with one-write and two-read ports
parameter M = 4; // number of address bits
parameter N = 16; // number of words, N = 2^M
parameter W = 8; // number of bits in a word
input clk, wr_enable;
input [W-1:0] din;
output [W-1:0] douta, doutb;
input [M-1:0] rd_addra, rd_addrb, wr_addr;
reg [W-1:0] reg_file [N-1:0];
…
assign douta = reg_file[rd_addra];
assign doutb = reg_file[rd_addrb];
always @(posedge clk)
if (wr_enable) reg_file[wr_addr] <= din;
1 word = 8bits
16 words

## Slide 41: A Register File (having 16 8-bit Words)
// an N-word register file with one-write and two-read ports
parameter M = 4; // number of address bits
parameter N = 16; // number of words, N = 2^M
parameter W = 8; // number of bits in a word
input clk, wr_enable;
input [W-1:0] din;
output [W-1:0] douta, doutb;
input [M-1:0] rd_addra, rd_addrb, wr_addr;
reg [W-1:0] reg_file [N-1:0];
…
assign douta = reg_file[rd_addra];
assign doutb = reg_file[rd_addrb];
always @(posedge clk)
if (wr_enable) reg_file[wr_addr] <= din;
din
douta
doutb
wr_addr
rd_addra
rd_addrb
wr_enable
clk

## Slide 42: A Register File
// an N-word register file with one-write and two-read ports with read_en
parameter M = 4; // number of address bits
parameter N = 16; // number of words, N = 2^M
parameter W = 8; // number of bits in a word
input clk, wr_enable, read_en_a, read_en_b;
input [W-1:0] din;
output [W-1:0] douta, doutb;
input [M-1:0] rd_addra, rd_addrb, wr_addr;
reg [W-1:0] reg_file [N-1:0];
…
assign douta = read_en_a ? _________________________;
assign doutb = read_en_b ? _________________________;
always @(posedge clk)
if (wr_enable) reg_file[wr_addr] <= din;
din
douta
doutb
wr_addr
rd_addra
rd_addrb
wr_enable
clk
read_en_a
read_en_b

## Slide 43: Register File
A key component in CPU
A set of registers + Mux/DeMux
[Intel] [http://fourier.eng.hmc.edu/e85_old/lectures/figures/register_file_diagram_0.gif]

## Slide 44: A Synchronous RAM (Random Access Memory)
// a synchronous RAM module example
parameter N = 16; // number of words
parameter A = 4; // number of address bits
parameter W = 8; // number of wordsize in bits
input [A-1:0] addr;
input [W-1:0] din;
input cs, wr, clk; //chip select, read-write control, and clock signals
output reg [W-1:0] dout;
reg [W-1:0] ram[N-1:0]; // declare an N * W memory array
always @(posedge clk)
if (cs) begin
if (wr) ram[addr] <= din;
else dout <= ram[addr];
end

## Slide 45: Sequential Logic
Flip-flops
Memory elements
Shift registers
Counters

## Slide 46: Shift register
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Holds samples of input
  store last 4 input values in sequence
  4-bit shift register:
One of the relatively simple registers is a shift register. Here one bit is shifted (or moved to right) to the next FF at each clock tick (its positive edge). At each positive edge, the stored value will come out and move to the next element.

## Slide 47: Shift register application
parallel inputs
parallel outputs
serial transmission
Parallel-to-serial conversion for serial transmission
One of the popular applications of the shift register is serial transmission, where information is transmitted over the medium bit-by-bit.

## Slide 48: Shift Registers

## Slide 49: Shift Registers
// a shift register module example
module shift_register(clk, reset_n, sin, qout);
parameter N = 4; // number of bits
input clk, reset_n, sin;
output reg [N-1:0] qout;
always @(posedge clk or negedge reset_n)
if (!reset_n) qout <= {N{1'b0}};
else qout <= {sin, qout[N-1:1]};
endmodule

## Slide 50: Shift Registers
// a shift register with parallel load module example
module shift_register_parallel_load (clk, load, reset_n, sin, din, qout);
parameter N = 8; // number of bits
input clk, load, reset_n, sin;
input [N-1:0] din;
output reg [N-1:0] qout;
always @(posedge clk or negedge reset_n)
if (!reset_n) qout <= {N{1'b0}};
else if (load) qout <= din;
else qout <= {sin, qout[N-1:1]};

## Slide 51: Universal Shift Registers

## Slide 52: Universal Shift Registers
// a universal shift register module
module universal_shift_register (clk, reset_n, s1, s0, lsi, rsi, din, qout);
parameter N = 4; // define the default size
input clk, reset_n, s1, s0, lsi, rsi;
input [N-1:0] din;
output reg [N-1:0] qout;
always @(posedge clk or negedge reset_n)
if (!reset_n) qout <= {N{1'b0}};
else case ({s1,s0})
2'b00: ; // qout <= qout; // No change
2'b01: qout <= {lsi, qout[N-1:1]}; // Shift right
2'b10: qout <= {qout[N-2:0], rsi}; // Shift left
2'b11: qout <= din; // Parallel load
endcase
endmodule

## Slide 53: Pattern recognizer
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
OUT
Combinational function of input samples
  in this case, recognizing the pattern 1001 on the single input signal
Another useful application of shift registers is bit string identification. In this case, bits are shifted from left to right. At any moment, if 4 bits are 1001, then OUT will be true.

## Slide 54: Sequential Logic
Flip-flops
Memory elements
Shift registers
Counters

## Slide 55: Binary Ripple Counters

## Slide 56: Binary Ripple Counters
// a 3-bit ripple counter module example
module ripple_counter(clk, qout);
input clk;
output reg [2:0] qout;
wire c0, c1;
// the body of the 3-bit ripple counter
assign c0 = qout[0], c1 = qout[1];
always @(negedge clk)
qout[0] <= ~qout[0];
always @(negedge c0)
qout[1] <= ~qout[1];
always @(negedge c1)
qout[2] <= ~qout[2];
C0
C1
C0
C1

## Slide 57: Binary Ripple Counters
// a 3-bit ripple counter with enable control
module ripple_counter_enable(clk, enable, reset_n, qout);
input clk, enable, reset_n;
output reg [2:0] qout;
wire c0, c1;
assign c0 = qout[0], c1 = qout[1];
always @(posedge clk or negedge reset_n)
if (!reset_n) qout[0] <= 1'b0;
else if (enable) qout[0] <= ~qout[0];
always @(posedge c0 or negedge reset_n)
if (!reset_n) qout[1] <= 1'b0;
else if (enable) qout[1] <= ~qout[1];
always @(posedge c1 or negedge reset_n)
if (!reset_n) qout[2] <= 1'b0;
else if (enable) qout[2] <= ~qout[2];

## Slide 58: Binary Ripple Counters
// an N-bit ripple counter using generate blocks
parameter N = 4; // define the size of counter
…
output reg [N-1:0] qout;
genvar i;
generate for (i = 0; i < N; i = i + 1) begin: ripple_counter
if (i == 0) // specify LSB
always @(negedge clk or negedge reset_n)
if (!reset_n) qout[0] <= 1'b0; else qout[0] <= ~qout[0];
else // specify the rest bits
always @(negedge qout[i-1] or negedge reset_n)
if (!reset_n) qout[i] <= 1'b0; else qout[i] <= ~qout[i];
end endgenerate

## Slide 59: Binary Up/Down Counters
module updn_bincounter (clk, reset, eup, edn, qout, cout, bout);
parameter N = 4;
input clk, reset, eup, edn;
output reg [N-1:0] qout;
output cout, bout;
always @(posedge clk)
if (reset) qout <= {N{1'b0}}; // synchronous reset
else if (eup) qout <= qout + 1;
else if (edn) qout <= qout - 1;
assign #1 cout = (&qout)& eup; // generate carry out
assign #1 bout = (~|qout)& edn; // generate borrow out

## Slide 60: Ring counters
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Sequences through a fixed set of patterns
  in this case, 1000, 0100, 0010, 0001
  if one of the patterns is its initial state (by loading or set/reset)
If there are multiple patterns that are used for state representation, this register is typically referred to as a counter. Look at the shift register in the slide. Suppose there is a initialization (or preset) logic that stores 1000 in the register, which is not shown here. Then, as the clock ticks, the bits are rotating this ring. That’s why it is called a ring counter.
1
0
0
0

## Slide 61: Ring counters
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Sequences through a fixed set of patterns
  in this case, 1000, 0100, 0010, 0001
  if one of the patterns is its initial state (by loading or set/reset)
If there are multiple patterns that are used for state representation, this register is typically referred to as a counter. Look at the shift register in the slide. Suppose there is a initialization (or preset) logic that stores 1000 in the register, which is not shown here. Then, as the clock ticks, the bits are rotating this ring. That’s why it is called a ring counter.
1
0
0
0

## Slide 62: Ring counters
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Sequences through a fixed set of patterns
  in this case, 1000, 0100, 0010, 0001
  if one of the patterns is its initial state (by loading or set/reset)
If there are multiple patterns that are used for state representation, this register is typically referred to as a counter. Look at the shift register in the slide. Suppose there is a initialization (or preset) logic that stores 1000 in the register, which is not shown here. Then, as the clock ticks, the bits are rotating this ring. That’s why it is called a ring counter.
1
0
0
0

## Slide 63: Activity
How does this counter work? (initial value: 1000)
D
Q
D
Q
D
Q
D
Q
IN
OUT1
OUT2
OUT3
OUT4
CLK
Counts through the sequence: 1000, 1100, 1110, 1111, 0111, 0011, 0001, 0000
Known as Mobius (or Johnson) counter

## Slide 64: Four-bit binary synchronous up-counter
EN D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
(1) Low order 4-bits = 1111
(2) RCO goes high
(3) High order 4-bits are incremented
Standard component with many applications
  positive edge-triggered FFs w/ synchronous load and clear inputs
  parallel load data from D, C, B, A
  enable inputs: must be asserted to enable counting
  ripple-carry out (RCO) is used for cascading counters
    high when counter is in its highest state 1111
    implemented using an AND gate
If we use the binary counter in the previous slide as a basic component, we can build many complicated circuits, e.g. a wider binary counter. Here D is the MSB.
Preset
logic

## Slide 65: Offset counters
Starting offset counters – use of synchronous load
  e.g., 0110, 0111, 1000, 1001, 1010, 1011, 1100, 1101, 1111, 0110, . . .
Ending offset counter – comparator for ending value
  e.g., 0000, 0001, 0010, ..., 1100, 1101, 0000
Combinations of the above (start and stop value)
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "0" "0" "0"
"0"
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "1" "1" "0"
Other examples are here; using the load input, we can control the initial value. Or by using some product term from the stored values, we can configure the ending value of the counter.

## Slide 66: Activity
Design a 4-bit incrementing counter whose values range between 0010 and 1110
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "0" "0" "0"
?
?
?

## Slide 67: Activity
Design a 4-bit incrementing counter whose values range between 0010 and 1110
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "0" "0" "0"
?
?
?
EN
D C B A
LOAD
CLK
CLR
RCO
QD QC QB QA
"1"
"0" "0" “1" "0"

## Slide 68: Design of a 4-bit incrementing counter (0010 ~ 1110) in Verilog
수범 여기 앞의 예제에 대한 Verilog code 추가하기 바래

## Slide 69: ALU + Register File in CPU Design
수범, term project으로 설계하는 CPU의 ALU 부분과 register file을 여기서 공부하게 하려고 해
ALU in Verilog
  Term project에서 쓰는 것과 조금 다르게
Register file in Verilog
  Term project에서 쓰는 것과 조금 다르게
Top에서 이 2개를 연결하고 test bench에서 ALU와 Register File에 control signal을 보내는 예제 코드 준비해 주기 바래

## Slide 70: Metastability and Asynchronous inputs
Clocked synchronous circuits
  Inputs, state, and outputs sampled or changed in relation to a common reference signal (called the clock)
  E.g., master/slave, edge-triggered
Asynchronous circuits
  Inputs, state, and outputs sampled or changed independently of a common reference signal (glitches/hazards a major concern)
  E.g., R-S latch
Asynchronous inputs to synchronous circuits
  Inputs can change at any time, will not meet setup/hold times
  Dangerous, synchronous inputs are greatly preferred
  Cannot be avoided (e.g., reset signal, memory wait, user input)

## Slide 71: Typical timing specifications
This slide illustrates the timing where the rising edge of the clock signal is the reference. Tpd is the propagation delay between the rising edge of the clock (event trigger) and the change in the output. Tw should be long enough to ensure that D will change Q
all measurements are made from the clocking event (the rising edge of the clock)
Positive edge-triggered D flip-flop
  setup (Tsu) and hold (Th) times
  Tpd: propagation delays (low to high, high to low, max and typical)
  Clock period > Tsu + Tpd
D
Clk
Q
T
su
1.8
ns
T
h
0.5
ns
T
w
3.3
ns
T
pd
3.6 ns
1.1 ns
T
su
1.8
ns
T
h
0.5
ns
T
pd
3.6 ns
1.1 ns
T
w
3.3
ns

## Slide 72: Timing Methodologies
clock
data1 & 2
changing
stable
F/F-controlled system (positive edge triggered)
clock
data1
D
Q
D
Q
data2
Positive edge-triggered
Setup time violation
Hold time violation

## Slide 73: Handling Asynchronous Inputs
In is asynchronous and fans out to D0 and D1 one FF catches the signal, one does not
inconsistent state may be reached!
In
Q0
Q1
CLK
What can go wrong?
  Input changes too close to clock edge (violating setup time constraint)
D
Q
D
Q
Q0
Clock
Clock
Q1
In
Tsu
Th

## Slide 74: Synchronization Failure
small, but non-zero probability that the FF output will get stuck in an in-between state
oscilloscope traces demonstrating
synchronizer failure and eventual
decay to steady state
logic 0
logic 1
logic 0
logic 1
Occurs when FF input changes close to clock edge
  FF may enter a metastable state – neither a logic 0 nor 1 –
  May stay in this state an indefinite amount of time
  Is not likely in practice but has some probability

## Slide 75: Dealing with Synchronization Failure
D
D
Q
Q
asynchronous
input
synchronized
input
synchronous system
Clk
Probability of failure can never be reduced to 0, but it can be reduced
  (1) slow down the system clock: this gives the synchronizer more time to decay into a steady state; synchronizer failure becomes a big problem for very high speed systems
  (2) use fastest possible logic technology in the synchronizer: this makes for a very sharp "peak" upon which to balance
  (3) cascade two synchronizers: this effectively synchronizes twice (both would have to fail)

## Slide 76: Handling Asynchronous Inputs
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
D
Q
Q0
Clock
Clock
Q1
Async
Input
D
Q
Clocked
Synchronous
System
Synchronizer
Never allow asynchronous inputs to fan-out to more than one flip-flop
  Synchronize as soon as possible and then treat as synchronous signal

## Slide 77: Sequential logic summary
Fundamental building block of circuits with state
  latch and flip-flop
  R-S latch, R-S master/slave, D master/slave, edge-triggered D flip-flop
Timing methodologies
  use of clocks
  Setup and hold times around the clock edge
Basic registers
  shift registers
  counters

## Slide 78: Appendix

## Slide 79: Storage Elements
Latch and flip-flop
  Register file, pipe stage, …
SRAM (static random access memory)
  Cache or large register file
DRAM (dynamic random access memory)
  Main memory or large cache
Flash memory
  Storage
Memory in Computer System
Register
file
Fetch/decode
ALU
LD/ST
Inst cache
Data cache
L2 cache
L3 cache
Main memory
Storage
CPU
WL
BL
WL
BL
WL
WL
BL
BL

## Slide 82: DRAM Scaling Limit
Year | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
DRAM ½ Pitch (nm) | 45 | 40 | 36 | 32 | 28 | 25 | 23 | 20 | 18 | 16 | 14
Manufacturable sol. | Exist |  |  | Known |  |  |  | NOT known |  |  | 
[ITRS, 2010]
p-type Si sub.
cap
n+
poly-Si
gate
n+
source
n+
drain
 RCAT DRAM Structure
 Capacitor lean (Cylinder > 2 um)
1.6 μm
> 2.0 μm
scalability limit: < 15 nm

## Slide 83: Intel 3D XPoint

## Slide 84: Phase-change RAM (PCM)
top
electrode
GST
metal
bit line
select TR
current
pulse
source
memory
VCC
Vgate
(Pictures from Hegedüs and Elliott, Nature Materials, March 2008)
Amorphous = high resistivity
Crystalline = low resistivity
SET
RESET

## Slide 85: Appendix

## Slide 86: What is HDL / Verilog
Why use HDL (Hardware Description Language)?
  Design can be described at a very abstract level
  Functional verification can be done early in the design cycle
  Reduce cost and time to design hardware
Verilog is one of the most popular HDLs
  Allowing different levels of abstraction in the same module
  A general-purpose, easy to learn, and easy to use HDL language
Key features of Verilog
  Supports various levels of abstraction
    Behavior level
    Register transfer level
    Gate level
  Simulate design functions
  Combines structural and behavioral modeling styles

## Slide 87: HDL-Based Design Flow
Hardware Specification Using C or Matlab
Behavioral/RTL Modeling (HDL)
Functional Simulation
Synthesis
Gate-level Simulation
Place & Route
Verify timing constraints
Bit-stream Generation
FPGA test
ASIC Design
Coverage in our practice class

## Slide 88: Number Representation
<size><base format><number>
  <size> : Number of bits (optional)
  <base format> : Single character (b, d, o, and h)
  <number> : Contains digits which are legal for the <base format>
Examples
  549 // decimal number
  ‘h8FF // hex number
  ‘o765 // octal number
  4’b11 // 4-bit binary number 0011
  3’b10x // 3-bit binary number with least significant bit unknown
  5’d3 // 5-bit decimal number
  -4’b11 // 4-bit two’s complement of 0011, or equivalently 1101

## Slide 89: Number Representation
Sized number
  <size>`<base format><number>
  4`b1001
  16`habcd
Unsized number: 32bit
`<base format><number>
  2009
  `habc
x or z
  x: an unknown value
  z: a high impedance

## Slide 90: Number Representation
Verilog’s nets and registers hold four-valued data
  0
    Obvious, logic 0, false condition
  1
    Obvious, logic 1, true condition
  Z
    Output of an undriven tri-state driver
    Models case where nothing is setting a wire’s value
  X
    Models when the simulator can’t decide the value
    Initial state of registers
    When a wire is being driven to 0 and 1 simultaneously
    Output of a gate with Z inputs

## Slide 91: Two Main Data Types
Nets(wire) represent connections between things
  Do not hold their value
  Take their value from a driver such as a gate or other module
  Cannot be assigned in an initial or always block
Regs(reg) represent data storage
  Behave exactly like memory in a computer
  Hold their value until explicitly assigned in an initial or always block
  Never connected to something
  Can be used to model latches, flip-flops, etc.
  Shared variables with all their attendant problems
  A variable of type register does not necessary represent a physical register

## Slide 92: The integer and time Variables
Integer variable
  Contains integer values
  Has at least 32 bits
  Is treated as a signed reg variable
    integer i, j;
    integer data[7:0];
Time variable
  Used for storing and manipulating simulation time
  Used in conjunction with the $time system task
  Only unsigned value and at least 64 bits
    time events;
    time current_time;

## Slide 93: Data Declaration
Size of register or wire
  reg [0:7] A, B; // A and B are 8-bit wide with MSB as 0th bit
  wire [3:0] Dout; // Dout is a 4-bit wire
  reg [7:0] C; // C is 8-bit register with MSB as the 8th bit
Assignments and concatenations
  A = 8’b0101_1010;
  B = {A[3:0] | A[7:4], 4’b0000};
  B is set to the 1st 4-bit of A bitwise or-ed with the last 4-bit of A and then concatenated with 0000.
  {} brackets means the bits of the 2 or more arguments separated by commas are concatenated together.

## Slide 94: Vectors
A vector = multiple bit width
  [high:low] or [low:high]
  The leftmost bit is the MSB
  include nets and reg data types
A scalar = 1-bit vector
Array and Memory Elements
  All net and variable data types are allowed
  An array element can be a scalar or a vector
wire a[3:0];
reg d[7:0];
wire [7:0] x[3:0];
reg [31:0] y[15:0];
integer states [3:0];
time current[5:0];

## Slide 95: Memory
reg [7:0] mema [7:0];
reg [7:0] memb [3:0][3:0];
wire sum [7:0][3:0];
mema[4][3]
mema[5][7:4]
memb[3][1][1:0]
sum[5][0]
Memory
  model ROM, RAM, or register files

## Slide 96: ‘assign’
Lvalue, Rvalue
  Lvalue: wire
  Rvalue: wire, reg
Connecting wire physically

## Slide 97: Basic Grammars
Describe a system by a set of modules
  Equivalent to functions in ‘C’
Keywords
  E.g., module, are reserved in all lower case letter
Operators (some examples)
  Arithmetic: +, -, *, /, !, ~
  Binary operators: &, |, ^, ~(bitwise), !(logical)
  Shift: <<, >>
  Relational: <, <=, >, >=, ==, !=
  Logical: &&, ||
Identifiers
  Equivalent to variable names
  Identifiers can be up to 1024 characters
Comments
  “//” for 1-line or /* to */ across several lines

## Slide 98: Operators

## Slide 99: Synthesizable Operators

## Slide 100: Arithmetic Operators
-10/5 // -2
-`d10 / 5 // (2’s complement of 10) / 5 = (232-10) / 5
The result is x if any operand bit has a value x
Negative numbers except integer variable are represented as 2’s complement

## Slide 101: Bitwise Operators
A bit-by-bit operation
  A z is treated as x
  The shorter operand is zero-extended

## Slide 102: An Example: A 4-to-1 MUX
// using basic and, or , not logic operators
assign out = (~s1 & ~s0 & i0) |
(~s1 & s0 & i1) |
(s1 & ~s0 & i2) |
(s1 & s0 & i3) ;

## Slide 103: Logical Operators
// A = 4'b1010,
B = 4'b1000
X | Y // 4’b1010
X || Y // 1
X & Y // 4’b1000
X && Y // 1
Always evaluate to a 1-bit value, 0, 1, or x
The result is x (a false condition) if any operand bit is x or z

## Slide 104: Concatenation/Replication Operators
Concatenation operator
y = {a, b[0], c[1]};
only for sized operand
Replication operator
y = {a, {4{b[0]}}, c[1]}; // y = {a, b[0], b[0], b[0], b[0], c[1]};

## Slide 105: An Example: A 4-Bit Full Adder
module full_adder (c_out, sum, x, y); input x, y; output c_out, sum;
// specify the function of a 4-bit adder
assign {c_out, sum} = x + y + c_in;
endmodule

## Slide 106: An Example: A 4-Bit Two’s Complement Adder
// specify the function of a two's complement adder
assign t = y ^ {4{c_in}};
assign {c_out, sum} = x + t + c_in;

## Slide 107: Reduction Operators
Perform only on one vector operand
  Carry out a bit-wise operation
  Yield a 1-bit result
  Work bit by bit from right to left

## Slide 108: An Example: A 9-Bit Parity Generator
// dataflow modeling using reduction operator
assign ep = ^x; // even parity generator
assign op = ~^ep; // odd parity generator

## Slide 109: An Example: An All-Bit-Zero/One Detector
// dataflow modeling
assign zero = ~(|x); // all-bit zero
assign one = &x; // all-bit one

## Slide 110: Relational Operators
The result is 1 if the expression is true and 0 if the expression is false
  Return x if any operand bit is x or z

## Slide 111: Equality Operators
Compare the two operands bit by bit
  The shorter operand is zero-extended
  Return 1 if the expression is true / 0 if the expression is false
  The operators (==, !=)
    yield an x if any operand bit is x or z
  The operators (===, !==)
    yield 1 if the two operands exactly match (‘x’ is also compared)
    0 if the two operands not exactly match

## Slide 112: Shift Operators
Logical shift operators
  0 is added in empty space
Arithmetic shift operators
  0(<<<) or MSB(>>>) is added in empty space

## Slide 113: Conditional Operator
assign out = selection ? in_1: in_0;
Usage: condition_expr ? true_expr: false_expr;
  If condition_expr = x or z: the result = true_expr & false_expr (0 and 0 gets 0, 1 and 1 gets 1, others gets x )
Nesting is allowed
  True_expr or Flase_expr can have condition
For example

## Slide 114: An Example: A 4-to-1 MUX
// using conditional operator (?:)
assign out = s1 ? ( s0 ? i3 : i2) : (s0 ? i1 : i0) ;

## Slide 115: Operator Precedence
Operators | Operator Symbol | Precedence
Unary Multiply, Divide, Modulus | + - ! ~ * / % | Highest
Add, Subtract Shift | + - << >> | 
Relational Equality | < <= > >= == != === !== | 
Reduction Logical | &, ~& ^, ~^ ¦, ~¦ && ¦ ¦ | 
Conditional | ? : | Lowest

## Slide 116: Synthesizable Operators

## Slide 117: An initial Block
Execute exactly once during simulation
Start at simulation time 0 &
Operate independently (Parallel)
reg x, y, z;
initial begin // complex statement
x = 1`b0; y = 1`b1; z = 1`b0;
#10 x = 1`b1; y = 1`b1; z = 1`b1;
end
initial x = 1`b0; // single statement but not recommended

## Slide 118: An initial Block

## Slide 119: An always Block
reg clock;
initial clock = 1`b0; //clock initialization
//with initial
always #5 clock = ~clock; // cycle = 10, 100MHz
initial # 1000 $finish; // $finish with initial
Starts at simulation time 0
Executes continuously during simulation
Behavior modeling should be located inside of procedural constructs

## Slide 120: Procedural Assignments
Syntax
variable_lvalue = [timing_control] expression
variable_lvalue <= [timing_control] expression
[timing_control] variable_lvalue = expression
[timing_control] variable_lvalue <= expression
lvalue : reg, integer, real, time (not net!!)
Two types
  blocking
  non-blocking

## Slide 121: Blocking Assignments
// blocking assignments
initial begin
x = #5 1'b0; // at time 5
y = #3 1'b1; // at time 8
z = #6 1'b0; // at time 14
end
Are executed in the specified order
Use the “=“ operator
Similar with C code

## Slide 122: An Example: Blocking Assignments

## Slide 123: Non-Blocking Assignments
reg x, y, z;
// nonblocking assignments
initial begin
x <= #5 1'b0; // at time 5
y <= #3 1'b1; // at time 3
z <= #6 1'b0; // at time 6
end
Use the “<=“ operator
  Same with operator “<=“, distinguish by used position
Used to model several concurrent data transfers

## Slide 124: An Example: Non-Blocking Assignments

## Slide 125: Intra-Assignment Delay Control
y = #25 ~x; // assign to y at time 25
count = #15 count + 1; // assign to count at time 40
y <= #25 ~x; // assign to y at time 25
count <= #15 count + 1; // assign to count at time 15
Intra-assignment delay control
  Defers the assignment to the left-hand-side variable
  Right side is already calculated

## Slide 126: An Example: A 4-Bit Full Adder
module full_adder (c_out, sum, x, y); input x[3:0], y[3:0]; output c_out, sum[3:0];
// specify the function of a 4-bit adder
// #5 assign {c_out, sum} = x + y + c_in;
assign {c_out, sum} = #5 x + y + c_in;
endmodule