## Slide 1: Chapter 8 FSM Minimization
Fall 2018
Logic Design
CSE, SNU

## Slide 2: Schedule

## Slide 3: Example: Vending Machine
Suitable Abstract Representation
  Tabulate typical input sequences:
    3 nickels
    nickel, dime
    dime, nickel
    two dimes
  Draw state diagram:
    Inputs: N, D, reset
    Output: open chute
  Assumptions:
    Assume N and D asserted for one cycle
    Each state has a self loop for N = D = 0 (no coin)
S0
Reset
S2
D
S6
[open]
D
S4
[open]
D
S1
N
S3
N
S7
[open]
N
S5
[open]
N

## Slide 4: Example: Vending Machine
State Diagram
S0
Reset
S2
D
S6
[open]
D
S4
[open]
D
S1
N
S3
N
S7
[open]
N
S5
[open]
N
present inputs next output state D N state open S0 0 0 S0 0 0 1 S1 0 1 0 S2 0 1 1 – – S1 0 0 S1 0 0 1 S3 0 1 0 S4 0 1 1 – – S2 0 0 S2 0 0 1 S5 0 1 0 S6 0 1 1 – – S3 0 0 S3 0 0 1 S7 0 1 – – – S4 – – S4 1 S5 – – S5 1 S6 – – S6 1 S7 – – S7 1
symbolic state table

## Slide 5: Example: Vending Machine
State Encoding and Truth Table
Present state inputs next state output Q2 Q1 Q0 D N D2 D1 D0 open 0 0 0 0 0 0 0 0 0 0 1 0 0 1 0 1 0 0 1 0 0 1 1 – – – – 0 0 1 0 0 0 0 1 0 0 1 0 1 1 0 1 0 1 0 0 0 1 1 – – – – 0 1 0 0 0 0 1 0 0 0 1 1 0 1 0 1 0 1 1 0 0 1 1 – – – – 0 1 1 0 0 0 1 1 0 0 1 1 1 1 0 1 – – – – – 1 0 0 – – 1 0 0 1 1 0 1 – – 1 0 1 1 1 1 0 – – 1 1 0 1 1 1 1 – – 1 1 1 1

## Slide 6: Example: Vending Machine
Implementation: D2, D1, D0, Open
D2 = Q2 + Q0·D + Q1·N + Q1·D
Open = Q2

## Slide 7: Example: Vending Machine
Implementation: D2

## Slide 8: Example: Vending Machine
Implementation: D1

## Slide 9: Example: Vending Machine
Implementation: D0

## Slide 10: Example: Vending Machine
Implementation: Open
13 gates + 3 F/Fs

## Slide 11: Example: Vending Machine (cont’d)
Minimize number of states - reuse states whenever possible
symbolic state table
present inputs next output state D N state open 0¢ 0 0 0¢ 0 0 1 5¢ 0 1 0 10¢ 0 1 1 – – 5¢ 0 0 5¢ 0 0 1 10¢ 0 1 0 15¢ 0 1 1 – – 10¢ 0 0 10¢ 0 0 1 15¢ 0 1 0 15¢ 0 1 1 – – 15¢ – – 15¢ 1
0¢
Reset
5¢
N
N
N
10¢
D
15¢
[open]
D

## Slide 12: Example: Vending Machine (cont’d)
present state inputs next state output Q1 Q0 D N D1 D0 open 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 0 1 1 – – – 0 1 0 0 0 1 0 0 1 1 0 0 1 0 1 1 0 1 1 – – – 1 0 0 0 1 0 0 0 1 1 1 0 1 0 1 1 0 1 1 – – – 1 1 – – 1 1 1
Uniquely Encode States
0¢
5¢
10¢
15¢

## Slide 13: Example: Vending Machine (cont’d)
Mapping to Logic
D1 = Q1 + D + Q0 N
D0 = Q0’ N + Q0 N’ + Q1 N + Q1 D
OPEN = Q1 Q0
0 0 1 1
0 1 1 1
X X X X
1 1 1 1
Q1
D1
Q0
N
D
0 1 1 0
1 0 1 1
X X X X
0 1 1 1
Q1
D0
Q0
N
D
0 0 1 0
0 0 1 0
X X X X
0 0 1 0
Q1
Open
Q0
N
D
13 gates + 3 F/Fs
8 gates + 2 F/Fs

## Slide 14: Finite State Machine Optimization
State Minimization
  Fewer states require fewer state bits
  Fewer bits require fewer logic equations
Encodings: State, Inputs, Outputs
  State encoding with fewer bits has fewer equations to implement
    However, each may be more complex
  State encoding with more bits (e.g., one-hot) has simpler equations
    Complexity directly related to complexity of state diagram
  Input/output encoding may or may not be under designer control

## Slide 15: State Minimization Example
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
Sequence Detector for 010 or 110
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0

## Slide 16: Algorithmic Approach to State Minimization
Goal – identify and combine states that have equivalent behavior
Equivalent States:
  Same output (behavior)
  For all input combinations, states transition to same or equivalent states
Row Matching Method: Algorithm Sketch
  1. Place all states in one set
  2. Initially partition set based on output behavior
  3. Successively partition resulting subsets based on next state transitions
  4. Repeat (3) until no further partitioning is required
    states left in the same set are equivalent
  Polynomial time procedure

## Slide 17: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
S1 is equivalent to S2
S3 is equivalent to S5
S4 is equivalent to S6

## Slide 18: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
S4 and S6 have the same
output behavior (1 0) and
state transition behavior (S0 S0)

## Slide 19: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 20: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 21: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
A
B
A
A
A
B
A
A
A
B
A
A
A
A
A
A

## Slide 22: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 23: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 24: Method of Successive Partitions
( S0 S1 S2 S3 S4 S5 S6 )
( S0 S1 S2 S3 S5 ) ( S4 S6 )
( S0 S3 S5 ) ( S1 S2 ) ( S4 S6 )
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1 S2 0 0
0 S1 S3 S4 0 0
1 S2 S5 S6 0 0
00 S3 S0 S0 0 0
01 S4 S0 S0 1 0
10 S5 S0 S0 0 0
11 S6 S0 S0 1 0
S1 is equivalent to S2
S3 is equivalent to S5
S4 is equivalent to S6
C
D
E
C
C
C
C
C
C
C
C
C
C
D
D
E
E

## Slide 25: Minimized FSM
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
State minimized sequence detector for 010 or 110
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )

## Slide 26: Minimized FSM
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
State minimized sequence detector for 010 or 110
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )

## Slide 27: Minimized FSM: A Simple Illustration
State minimized sequence detector for 010 or 110
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S2
S1
1/0
0/0
1/0
0/0
1/0
0/0
S3’
S4’
1/0
0/1
X/0
( S0 ) ( S3 S5 ) ( S1 S2 ) ( S4 S6 )

## Slide 28: Minimized FSM
State minimized sequence detector for 010 or 110
Input Next State Output
Sequence Present State X=0 X=1 X=0 X=1
Reset S0 S1' S1' 0 0
0 + 1 S1' S3' S4' 0 0
X0 S3' S0 S0 0 0
X1 S4' S0 S0 1 0
S0
S1’
S3’
S4’
X/0
1/0
1/0
0/1
0/0
X/0
S0
S3
S2
S1
S5
S6
S4
1/0
0/0
1/0
1/0
0/1
0/0
1/0
0/0
1/0
0/0
1/0
0/1
1/0
0/0
State
Minimization!

## Slide 29: Implication Chart Method
3-bit sequence detector example
  Take 3 bits as input. Output = 1 in case of 010 or 110

## Slide 30: Implication Chart Method: 3-bit seq. detector

## Slide 31: Implication Chart Method: 3-bit seq. detector
Check each equivalence candidate from top to down and left to right
For each candidate, check to see if the next states are the same for each transition
If not the same, cross out the candidate since the two states of the candidate have different state transition behavior

## Slide 32: Implication Chart Method: 3-bit seq. detector
Check each equivalence candidate from top to down and left to right
For each candidate, check to see if the next states are the same for each transition
If not the same, cross out the candidate since the two states of the candidate have different state transition behavior

## Slide 33: Implication Chart Method: 3-bit seq. detector
Check each equivalence candidate from top to down and left to right
For each candidate, check to see if the next states are the same for each transition
If not the same, cross out the candidate since the two states of the candidate have different state transition behavior

## Slide 34: Implication Chart Method: 3-bit seq. detector
Check each equivalence candidate from top to down and left to right
For each candidate, check to see if the next states are the same for each transition
If not the same, cross out the candidate since the two states of the candidate have different state transition behavior

## Slide 35: Results
S3=S5, S4=S6, S1=S2

## Slide 36: More Complex State Minimization
symbolic state transition table
present next state output state 00 01 10 11 S0 S0 S1 S2 S3 1 S1 S0 S3 S1 S4 0 S2 S1 S3 S2 S4 1 S3 S1 S0 S4 S5 0 S4 S0 S1 S2 S5 1 S5 S1 S4 S0 S5 0
inputs here
Multiple input example
10
01
11
00
00
01
11
10
10
01
11
00
10
00
11
00
11
10
01
10
11
01
00
S0 [1]
S2 [1]
S4 [1]
S1
[0]
S3
[0]
S5
[0]
01

## Slide 37: Minimized FSM
S0-S1
S1-S3
S2-S2
S3-S4
S0-S0
S1-S1
S2-S2
S3-S5
S0-S1
S3-S0
S1-S4
S4-S5
S0-S1
S3-S4
S1-S0
S4-S5
S1-S0
S3-S1
S2-S2
S4-S5
S4-S0
S5-S5
S1-S1
S0-S4
minimized state table
(S0==S4) (S3==S5)
present next state output state 00 01 10 11 S0' S0' S1 S2 S3' 1 S1 S0' S3' S1 S3' 0 S2 S1 S3' S2 S0' 1 S3' S1 S0' S0' S3' 0
Implication Chart Method
  Cross out incompatible states based on outputs
  Then cross out more cells if indexed chart entries are already crossed out
S1
S2
S3
S4
S5
S0
S1
S2
S3
S4

## Slide 38: Summary: Finite State Machine Optimization
State Minimization
  Fewer states require fewer state bits
  Fewer bits require fewer logic equations
Encodings: State, Inputs, Outputs
  State encoding with fewer bits has fewer equations to implement
    However, each may be more complex
  State encoding with more bits (e.g., one-hot) has simpler equations
    Complexity directly related to complexity of state diagram
  Input/output encoding may or may not be under designer control

## Slide 39: Schedule

## Slide 40: Exercise 8.5.
Implication chart method:

## Slide 41: Exercise 8.5.
Implication chart method:
    State B cannot be combined: different output

## Slide 42: Exercise 8.5.
Implication chart method:
  States cannot be combined which contains state B

## Slide 43: Exercise 8.5.
Implication chart method:
  After state minimization
A’  A, E
C’  C, F
D’  D, G

## Slide 44: Exercise 8.6.
Implication chart method:

## Slide 45: Exercise 8.6.
Implication chart method:
  States which have different outputs cannot be combined

## Slide 46: Exercise 8.6.
Implication chart method:
  States cannot be combined which contains states already excluded

## Slide 47: Exercise 8.6.
Implication chart method:
  States cannot be combined which contains states already excluded

## Slide 48: Exercise 8.6.
Implication chart method:
  After state minimization
S0’  S0, S6
S1’  S1, S2, S4, S5
1
0
0
1
S0
S1
S5
Can be combined

## Slide 49: Exercise 8.2.
Given the state diagram in Figure below, obtain an equivalent reduced-state diagram containing a minimum number of states. You may use row-matching or implication charts. Put your final answer in the form of a state diagram rather than a state table. Make it clear which states have been combined.

## Slide 50: Exercise 8.2.
State transition table

## Slide 51: Exercise 8.2.
Implication chart method:
  D cannot be equivalent to any others: different output behavior

## Slide 52: Exercise 8.2.
Implication chart method:
  Cross out cells exploiting the fact that state D cannot be equivalent to any other state

## Slide 53: Exercise 8.2.
Implication chart method:
  States in these state pairs cannot be combined due to the inequivalent states revealed in the previous cells

## Slide 54: Exercise 8.2.
Implication chart method:
  Final implication chart  State A and B can be combined
   State E, F and G can be combined
0
1
1
0
C
A
B
Can be combined
1
0
0
AB
E
F
G
1
1
0
Can be combined

## Slide 55: Exercise 8.2.
Implication chart method:
  State diagram for minimized states

## Slide 56: Exercise 8.4.
Given the state diagram in figure below, determine which states should be combined to determine the reduced state diagram. You may use row-matching or implication charts.

## Slide 57: Exercise 8.4.
State transition table

## Slide 58: Exercise 8.4.
Implication chart method:
  State S6 cannot be combined: different output

## Slide 59: Exercise 8.4.
Implication chart method:
  States cannot be combined which contains state S6

## Slide 60: Exercise 8.4.
Implication chart method:
  States cannot be combined which contains states already excluded, e.g., S2

## Slide 61: Exercise 8.4.
Implication chart method:
  Final implication chart
  S1=S5, S0=S4
1
0
0
1
S1,5
S3
S4
Can be combined

## Slide 62: Exercise 8.4.
State diagram for minimized states

## Slide 63: Exercise 8.3.
Create a Moore state diagram for the 4-bit string recognizer of figure below. Does it have more states than the Mealy version? Use the implication chart method to reduce the number of states. Do you end with more, less, or the same number of states? Why?

## Slide 64: Exercise 8.3.
State transition table

## Slide 65: Exercise 8.3.
State transition table

## Slide 66: Exercise 8.3.
Implication chart method:
  State S10 and S12 should be combined only with each other
    Different output

## Slide 67: Exercise 8.3.
Implication chart method:
  States cannot be combined which contains state S10 or S12
    Except S12 or S10

## Slide 68: Exercise 8.3.
Implication chart method:
  States cannot be combined which contains states already excluded
    State S4 and S5 should be combined only with each other

## Slide 69: Exercise 8.3.
Implication chart method:
  States cannot be combined which contains states already excluded
    State S1 or S2 cannot be combined with other states

## Slide 70: Exercise 8.3.
Implication chart method:
  States cannot be combined which contains states already excluded
    State S0 cannot be combined with other states

## Slide 71: Exercise 8.3.
Implication chart method:
  S3, S6 can be combined
  S4, S5 can be combined
  S7, S8, S9, S11, S13, S14 can be combined
  S10, S12 can be combined

## Slide 72: Exercise 8.3.
State diagram before state minimization

## Slide 73: Exercise 8.3.
State diagram for minimized states