## Slide 1: Chapter 5 Case studies in combinational logic design
Now we have gone through every part of combinational logic system design.
In this chapter, the final chapter of combination logic, we will look at some examples and elaborate on the whole design process.

## Slide 2: Schedule (by Mid-term Exam)

## Slide 3: Combinational logic design case studies
General design procedure
Case studies
  BCD to 7-segment display controller
  logical function unit
  process line controller
  calendar subsystem
Arithmetic circuits
  integer representations
  addition/subtraction
  arithmetic/logic units
I will talk about the steps of a general procedure to design a combinational logic system first and then take some examples.

## Slide 4: General design procedure for combi. logic
1. Understand the problem
  what is the circuit supposed to do?
  write down inputs (data, control) and outputs
  draw block diagram or other picture
2. Formulate the problem using a suitable design representation
  truth table or waveform diagram are typical
  may require encoding of symbolic inputs and outputs
3. Choose implementation target
  ROM, PAL, PLA
  mux, decoder and OR-gate
  discrete gates (fixed logic)
4. Follow implementation procedure
  K-maps for two-level, multi-level
  design CAD tools and hardware description language (e.g., Verilog)
Typically, we have to separate the I/O variables and system internals to understand the problem. Step 2 is abstract representation while steps 3 and 4 are H/W implementation dependent

## Slide 5: Tip: CAD tool’s typical functionalities
Design entry
  Truth table, schematic capture, HDL
Synthesis and optimization
Simulation
Physical design
First of all, a user of a CAD tool should be able to specify the requirements of a logic circuit to be designed. The requirements can be expressed by a truth table or a graphical drawing, or a language.
Synthesis usually refers to the process of translating designer’s requirements into a circuit graph.
Physical design transforms the circuit graph into a layout (or blueprint) for fabrication

## Slide 6: BCD to 7-segment display controller
BCD to 7–segment control signal decoder
c0 c1 c2 c3 c4 c5 c6
A B C D
Understanding the problem
  input is a 4 bit bcd digit (A, B, C, D)
  output is the control signals for the display (7 outputs C0 – C6)
Block diagram
c1
c5
c2
c4
c6
c0
c3
The first case is to control or display one digit system whose input follows BCD coding.
A digit can be represented by a combination of 7 segments. Depending on input variables, we have to turn on relevant pieces or segments.

## Slide 7: Formalize the problem
A B C D C0 C1 C2 C3 C4 C5 C6
0 0 0 0 1 1 1 1 1 1 0
0 0 0 1 0 1 1 0 0 0 0
0 0 1 0 1 1 0 1 1 0 1
0 0 1 1 1 1 1 1 0 0 1
0 1 0 0 0 1 1 0 0 1 1
0 1 0 1 1 0 1 1 0 1 1
0 1 1 0 1 0 1 1 1 1 1
0 1 1 1 1 1 1 0 0 0 0
1 0 0 0 1 1 1 1 1 1 1
1 0 0 1 1 1 1 0 0 1 1
1 0 1 – – – – – – – –
1 1 – – – – – – – – –
Truth table
  show don't cares
Choose implementation target
  if ROM, we are done
  don't cares imply PAL/PLA may be attractive
Follow implementation procedure
  minimization using K-maps or QM
How many input variables? And output variables?
If we use ROM for the implementation technology, then the game is over. What we need to do is just to store 7 bit values for each minterm, total 2**4 cases. Even though we need to use only 10 minterms, we have to use 2**4 AND gates, whose size is much bigger than other technologies. So we choose PAL or PLA, where minimum # of product terms are desirable. As there are DC terms, we may be able to reduce the size of the system by minimization in two-level logic design.

## Slide 8: Implementation as minimized sum-of-products
C0 = A + B D + C + B' D'
C1 = C' D' + C D + B'
C2 = B + C' + D
C3 = B' D' + C D' + B C' D + B' C
C4 = B' D' + C D'
C5 = A + C' D' + B D' + B C'
C6 = A + C D' + B C' + B' C
15 unique product terms when minimized individually
1 0 X 1
0 1 X 1 1 1 X X
1 1 X X
D
A
B
C
1 1 X 1
1 0 X 1 1 1 X X
1 0 X X
D
A
B
C
0 1 X 1
0 1 X 1 1 0 X X
1 1 X X
D
A
B
C
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
1 0 X 1
0 1 X 0 1 0 X X
1 1 X X
D
A
B
C
1 0 X 1
0 0 X 0 0 0 X X
1 1 X X
D
A
B
C
1 1 X 1
0 1 X 1 0 0 X X
0 1 X X
D
A
B
C
Here are the final two-level s-o-p forms for 7 output functions. After removing duplicate product terms, we have 15 different product terms to represent 7 outputs. We should note that the minimized form of each output may not lead to the globally minimum number of product terms. In this case, we have 15 product terms for 7 outputs
C0
C1
C2
C3
C4
C5
C6
8

## Slide 9: Implementation as minimized S-o-P (cont'd)
C0 = B C' D + C D + B' D' + B C D' + A C1 = B' D + C' D' + C D + B' D' C2 = B' D + B C' D + C' D' + C D + B C D' C3 = B C' D + B' D + B' D' + B C D' C4 = B' D' + B C D' C5 = B C' D + C' D' + A + B C D' C6 = B' C + B C' + B C D' + A
C0 = A + B D + C + B' D'
C1 = C' D' + C D + B'
C2 = B + C' + D
C3 = B' D' + C D' + B C' D + B' C
C4 = B' D' + C D'
C5 = A + C' D' + B D' + B C'
C6 = A + C D' + B C' + B' C
C2
Can do better
  9 unique product terms (instead of 15)
  share terms among outputs
  each output not necessarily in minimized form
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
1 1 X 1
1 1 X 1 1 1 X X
0 1 X X
D
A
B
C
C2
Let’s look at C2 output variable. If we relax the minimization process of C2, we have more terms for C2 output. However, this less efficient minimization achieves sharing more product terms in the overall system (7 outputs). Note that the number of product terms of each output increases. Can we figure out this globally optimal minimization?

## Slide 10: PLA implementation
BC'
B'C
B'D
BC'D
C'D'
CD
B'D'
A
BCD'
A B C D
C0 C1 C2 C3 C4 C5 C6 C7
Since there are up to 5 product terms for outputs, PAL (with 4 product terms per output) may not be attractive. There are many common terms; so PLA is a good choice.

## Slide 11: PAL implem. vs. Discrete gate implementation
Let’s consider PAL implementation where up to 4 product terms can be ORed. Unfortunately, there are outputs that have 5 product terms. In that case, we have to resort to multi-level logic. You don’t need to do that; the CAD tool will do the job.
C0 = C3 + A' B X' + A D Y
C1 = Y + A' C5' + C' D' C6
C2 = C5 + A' B' D + A' C D
C3 = C4 + B D C5 + A' B' X'
C4 = D' Y + A' C D'
C5 = C' C4 + A Y + A' B X
C6 = A C4 + C C5 + C4' C5 + A' B' C
X = C' + D'
Y = B' C'
Limit of 4 product terms per output
  decomposition of functions with larger number of terms
  do not share terms in PAL anyway (although there are some shared terms)
Decompose into multi-level logic (hopefully with CAD support)
  find common sub-expressions among functions
C2 = B + C' + D
C2 = B' D + B C' D + C' D' + C D + B C D'
C2 = B' D + B C' D + C' D' + W
W = C D + B C D'
need another input and another output

## Slide 12: Logical function unit
C0 C1 C2 Function Comments 0 0 0 1 always 1 0 0 1 A + B logical OR 0 1 0 (A • B)' logical NAND 0 1 1 A xor B logical xor 1 0 0 A xnor B logical xnor 1 0 1 A • B logical AND 1 1 0 (A + B)' logical NOR 1 1 1 0 always 0
3 control inputs: C0, C1, C2 2 data inputs: A, B 1 output: F
Multi-purpose function block
  3 control inputs to specify operation to perform on operands
  2 data inputs for operands
  1 output of the same bit-width as operands
The next example is the very versatile functional block, which performs various functions. There are three control variables whose values determine the output of the function of two data input variables.

## Slide 13: Formalize the problem
C0 C1 C2 A B F
0 0 0 0 0 1
0 0 0 0 1 1
0 0 0 1 0 1
0 0 0 1 1 1
0 0 1 0 0 0
0 0 1 0 1 1
0 0 1 1 0 1
0 0 1 1 1 1
0 1 0 0 0 1
0 1 0 0 1 1
0 1 0 1 0 1
0 1 0 1 1 0
0 1 1 0 0 0
0 1 1 0 1 1
0 1 1 1 0 1
0 1 1 1 1 0
1 0 0 0 0 1
1 0 0 0 1 0
1 0 0 1 0 0
1 0 0 1 1 1
1 0 1 0 0 0
1 0 1 0 1 0
1 0 1 1 0 0
1 0 1 1 1 1
1 1 0 0 0 1
1 1 0 0 1 0
1 1 0 1 0 0
1 1 0 1 1 0
1 1 1 0 0 0
1 1 1 0 1 0
1 1 1 1 0 0
1 1 1 1 1 0
choose implementation technology 5-variable K-map to discrete gates multiplexer implementation
1 0
A B
A B
A B
C2
C0
C1
0 1 2 3 4 5 6 7
S2
8:1 MUX
S1
S0
F
In order to realize the multi-purpose function, we combine discrete gates and an 8:1 MUX.

## Slide 14: Production line control
Rods of varying length (+/-10%) travel on conveyor belt
  mechanical arm pushes rods within spec (+/-5%) to one side
  second arm pushes rods too long to other side
  rods that are too short stay on belt
  3 light barriers (light source + photocell) as sensors
  design combinational logic to activate the arms
Understanding the problem
  inputs are three sensors
  outputs are two arm control signals
  assume sensor reads "1" when tripped
    "0" otherwise (if nothing to detect)
  call sensors A, B, C
The next case study to look at is a product line control (PLC) system that manufactures a rod. What we need to do is to check whether each rod’s length is within a certain bound (± 5% of the spec). In order to examine the length of each rod, we use three sensors to measure the rod. If the rod is within spec, the rod will be pushed to one side. If the rod is too long, it will be pushed to the other side. Otherwise, it will stay on the belt.

## Slide 15: Sketch of problem
Position of sensors
  A to B distance = specification – 5%
  A to C distance = specification + 5%
Within Spec
Too Short
Too Long
A
B
C
spec - 5%
spec + 5%
What if we don’t have sensor A? We cannot know the reference point or time at which we can measure the length of each rod. So when sensor A becomes 1, we should check sensors B and C as well to measure the length of the moving rod.

## Slide 16: Formalize the problem
logic implementation now straightforward just use three 3-input AND gates "too short" = AB'C' (only first sensor tripped) "in spec" = A B C' (first two sensors tripped)
"too long" = A B C (all three sensors tripped)
A B C Function 0 0 0 do nothing 0 0 1 do nothing 0 1 0 do nothing 0 1 1 do nothing 1 0 0 too short 1 0 1 don't care 1 1 0 in spec 1 1 1 too long
Truth table
  show don't cares
If A is zero, that means there is no rod to inspect. So all the outputs are 0.
Otherwise, there is a rod. Then we have to check sensors B and C. Note that 101 is a DC term. 110 means that the rod is of standard length. The textbook says the top 4 minterms (000 – 011) are also DC terms, but that may cause energy waste.

## Slide 17: Steps 3 and 4
Choose implementation technology
  The actual logic is so simple; use fixed logic gates
Follow implementation procedure
  One minterm for each output
So the truth table is done. As the overall logic is so simple. Maybe the random logic approach is the best. There are three outputs, each of which has only one minterm

## Slide 18: Calendar subsystem
integer number_of_days ( month, leap_year_flag) {
  switch (month) {
    case 1: return (31);
    case 2: if (leap_year_flag == 1)
    then return (29) else return (28);
    case 3: return (31);
    case 4: return (30);
    case 5: return (31);
    case 6: return (30);
    case 7: return (31);
    case 8: return (31);
    case 9: return (30);
    case 10: return (31);
    case 11: return (30);
    case 12: return (31);
    default: return (0);
  }
}
Determine number of days in a month (to control watch display)
  used in controlling the display of a wrist-watch LCD screen
  inputs: month, leap year flag
  outputs: number of days
Use software implementation to help understand the problem
For the next example, we revisit the number of days per month problem. But this time, we will follow the general procedure to design the system. Then we will look at the details of the leap year flag.

## Slide 19: Formalize the problem
leap
month
28
29
30
31
month leap 28 29 30 31 0000 – – – – – 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 0101 – 0 0 0 1 0110 – 0 0 1 0 0111 – 0 0 0 1 1000 – 0 0 0 1 1001 – 0 0 1 0 1010 – 0 0 0 1 1011 – 0 0 1 0 1100 – 0 0 0 1 1101 – – – – – 111– – – – – –
Again 4 wires for the input of month and one wire for leap year and 4 wires for the output (note that only two wires are needed for output at minimum)
Encoding:
  binary number for month: 4 bits
  4 wires for 28, 29, 30, and 31 one-hot – only one true at any time
Block diagram:

## Slide 20: Choose implem. target and perform mapping
month leap 28 29 30 31 0000 – – – – – 0001 – 0 0 0 1 0010 0 1 0 0 0 0010 1 0 1 0 0 0011 – 0 0 0 1 0100 – 0 0 1 0 0101 – 0 0 0 1 0110 – 0 0 1 0 0111 – 0 0 0 1 1000 – 0 0 0 1 1001 – 0 0 1 0 1010 – 0 0 0 1 1011 – 0 0 1 0 1100 – 0 0 0 1 1101 – – – – – 111– – – – – –
Discrete gates
  28 =
  29 =
  30 =
  31 =
Can translate to S-o-P or P-o-S
m8’ m4’ m2 m1’ leap’
m8’ m4’ m2 m1’ leap
m8’ m4 m1’ + m8 m1
m8’ m1 + m8 m1’
If we are to use discrete logic gates such as AND or OR, SoP or PoS will be enough.
Just investigate all the elements of the On-set, and make product terms and then combine them by OR gates in SoP case. From now on we will look at the leap year flag. How can we know that a year is a leap year or not?

## Slide 21: Leap year flag
Determine value of leap year flag given the year
  For years after 1582 (Gregorian calendar reformation),
  leap years are all the years divisible by 4,
  except that years divisible by 100 are not leap years,
  but years divisible by 400 are leap years.
Encoding the year:
  binary – easy for divisible by 4, 2006:1111101010
  but difficult for 100 and 400 (not powers of 2)
  BCD – easy for 100, 2006: 0010 0000 0000 0110 but more difficult for 4, what about 400?
Parts:
  construct a circuit that determines if the year is divisible by 4
  construct a circuit that determines if the year is divisible by 100
  construct a circuit that determines if the year is divisible by 400
  combine the results of the previous three steps to yield the leap year flag
Pope Gregory I set up the current leap year system in 1582. There are only three simple rules that decide the number of days in Feb. Note that an encoding scheme can affect the system design fundamentally.

## Slide 22: Activity: divisible-by-4 circuit
BCD coded year
  YM8 YM4 YM2 YM1 – YH8 YH4 YH2 YH1 – YT8 YT4 YT2 YT1 – YO8 YO4 YO2 YO1
Only need to look at low-order two digits of the year all years ending in 00, 04, 08, 12, 16, 20, etc. are divisible by 4
  if tens digit is even, then divisible by 4 if ones digit is 0, 4, or 8
  if tens digit is odd, then divisible by 4 if the ones digit is 2 or 6.
Translates into the following Boolean expression (where YT1 is the year's tens digit low-order bit, YO8 is the high-order bit of year's ones digit, etc.): YT1’ (YO8’ YO4’ YO2’ YO1’ + YO8’ YO4 YO2’ YO1’ + YO8 YO4’ YO2’ YO1’ ) + YT1 (YO8’ YO4’ YO2 YO1’ + YO8’ YO4 YO2 YO1’ )
Digits with values of 10 to 15 will never occur, simplify further to yield:
D4 = YT1’ YO2’ YO1’ + YT1 YO2 YO1’
YM stands for year millennium and the each digit of the year will be represented as the binary value by BCD encoding. So we need 4 wires for each digit of the year, total 16 wires. D4 is the flag that indicates whether the year of input is divisible by 4

## Slide 23: Divisible-by-100 and divisible-by-400 circuits
Divisible-by-100 just requires checking that all bits of two low-order digits are all 0: D100 = YT8’ YT4’ YT2’ YT1’ • YO8’ YO4’ YO2’ YO1’
Divisible-by-400 combines the divisible-by-4 (applied to the thousands and hundreds digits) and divisible-by-100 circuits D400 = (YM1’ YH2’ YH1’ + YM1 YH2 YH1’) • (YT8’ YT4’ YT2’ YT1’ • YO8’ YO4’ YO2’ YO1’ )
With BCD encoding, it is easy to check whether the year of input is divisible by 100 and 400. A year is divided by 100 without remainder if the lowest two digits are 00
A year is divided by 400 without residue if the lowest two digits are 00 and the highest two digits are divided by 4.

## Slide 24: Combining to determine leap year flag
Label results of previous three circuits: D4, D100, and D400 leap_year_flag = D4 • D100’ + D4 • D400 = D4 • D100’ + D400
Now we have three (internal) variables, each of which indicates whether the year is divisible by 4, 100, 400, respectively. The final leap year flag should be true when D4 is true. But if D100 is true than the flag is false. Note that the flag is also true when D4 and D400 is true

## Slide 25: Implementation of leap year flag

## Slide 26: Arithmetic circuits
Excellent examples of combinational logic design
Time vs. space trade-offs
  doing things fast may require more logic and thus more space
  example: carry lookahead logic
Arithmetic and logic units
  general-purpose building blocks
  critical components of processor datapaths
  used within most computer instructions
Now we are going to see a little bit different logic system, whose purpose is to perform a mathematical function. We will look at adders mostly.
In most of engineering systems, there is always a trade-off. We cannot have all the best features in a single system. As mentioned earlier, if we use a number of gates in parallel (say, two-level SoP canonical forms), we can minimize the delay of the system. If we want to reduce the number of gates, there will be multiple levels, which increases delay. We will revisit this issue by going over multiple variations of adder systems

## Slide 27: Number systems
Representation of positive numbers is the same in most systems
Major differences are in how negative numbers are represented
Representation of negative numbers come in three major schemes
  sign and magnitude
  1s complement
  2s complement
Assumptions
  we'll assume a 4 bit machine word
  16 different values can be represented
  roughly half are positive, half are negative
To design arithmetic functions, we have to understand how a number is represented in computers. We talked about binary coding, BCD coding and so on. Here we choose the binary coding as the basic representation system but will focus on how negative numbers are expressed.
For the purpose of illustration, we consider the case of using 4 wires to represent a digit (positive and negative and zero).

## Slide 28: Sign and magnitude
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
–0
–1
–2
–3
–4
–5
–6
–7
0 100 = + 4 1 100 = – 4
One bit dedicate to sign (positive or negative)
  sign: 0 = positive (or zero), 1 = negative
Rest represent the absolute value or magnitude
  three low order bits: 0 (000) thru 7 (111)
Range for n bits
  ±( 2n–1 –1) (two representations for 0)
Cumbersome addition/subtraction
  must compare magnitudes to determine sign of result
The first encoding scheme is sign and magnitude; one bit is dedicated to the sign of the number and the rest of the bits represents the absolute value of the number |x|. If we use 4 bits total, the MSB is the sign + or -, and the other three bits represent the magnitude from 0 to 7. The problem is that when adding or subtracting numbers, we have to check the sign of the results.

## Slide 29: 1s complement
2 = 10000
1 = 00001
2 –1 = 1111
7 = 0111
1000 = –7 in 1s complement form
4
4
If N is a positive number, then the negative of N (or its 1s complement) is N' = (2n –1) – N
  example: 1s complement of 7
  shortcut: simply compute bit-wise complement ( 0111 -> 1000 )
To remedy the sign-magnitude encoding problem, 1s complement is introduced. Here, a negative of N (which is –N) is denoted by N’ and is expressed by (2n-1)-N.
The 1st bit implicitly says the sign of the number. The merit of this encoding scheme is that subtraction becomes easier.

## Slide 30: 1s complement (cont'd)
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
–7
–6
–5
–4
–3
–2
–1
–0
0 100 = + 4 1 011 = – 4
Then, subtraction can be easily performed. To compute A-B, just calculate 1s complement of B and then add it to A. Actually this works only when B >= A. Look at the range from -7 to +7 and note that there are two kinds of 0s.
Subtraction implemented by 1s complement and then addition
Two representations of 0
  causes some complexities in addition
High-order bit can act as sign bit
Carry should be added to the sum

## Slide 31: 2s complement
0 100 = + 4 1 100 = – 4
+0
+1
+2
+3
+4
+5
+6
+7
–8
–7
–6
–5
–4
–3
–2
–1
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
1s complement with negative numbers shifted one position clockwise
  only one representation for 0
  one more negative number than positive numbers
  high-order bit can act as sign bit
2s compliment enhances the 1s complement encoding, it can represent up to -8 as shown in the above.

## Slide 32: 2s complement (cont’d)
2 = 10000
7 = 0111
1001 = repr. of –7
4
2 = 10000
–7 = 1001
0111 = repr. of 7
4
subtract
subtract
If N is a positive number, then the negative of N (or its 2s complement) is N* = 2n – N
  example: 2s complement of 7
  example: 2s complement of –7
  shortcut: 2s complement = bit-wise complement + 1
    0111 -> 1000 + 1 -> 1001 (representation of -7)
    1001 -> 0110 + 1 -> 0111 (representation of 7)
Likewise, the 2s compliment of a positive number N is denoted by N*. If you want to make a 2s complement in case of 4 wires, just subtract the number from 2**4. Another simple way to calculate 2s complements is to invert all the bits and add 1.

## Slide 33: 2s complement addition and subtraction
4
+ 3
7
0100
0011
0111
– 4
+ (– 3)
– 7
1100
1101
11001
4
– 3
1
0100
1101
10001
– 4
+ 3
– 1
1100
0011
1111
Simple addition and subtraction
  simple scheme makes 2s complement the virtually unanimous choice for integer number systems in computers
Let’s see how we can add or subtract the numbers encoded by 2s complement. Now subtraction is not so different from addition. Just make 2s complement and add it.

## Slide 34: Why can the carry-out be ignored?
Can't ignore it completely
  needed to check for overflow (see next two slides)
When there is no overflow, carry-out may be true but can be ignored – M + N when N > M: M* + N = (2n – M) + N = 2n + (N – M) ignoring carry-out is just like subtracting 2n – M + – N where N + M  2n-1 (– M) + (– N) = M* + N* = (2n– M) + (2n– N) = 2n – (M + N) + 2n ignoring the carry, it is just the 2s complement representation for – (M + N)
So far, we didn’t pay attention to the carry. We will first look at the cases where carry-outs can be ignored. Let M be the positive number to be converted by 2s complement. M* denotes 2s complement of M, which is 2n-M.

## Slide 35: Overflow in 2s complement addition / subtraction
There are two kinds of overflows in 2s complement arithmetic. In this case, the carry-out should not be ignored. The upper bound in 4 bits is +7; so when the sum exceeds this bound, there will be an overflow. Likewise, the lower bound is -8; so when the sum goes below -8, there is an overflow, which is also called underflow. Anyway, in these overflow cases, the adding system should report the error.
5 + 3 = –8
–7 – 2 = +7
+0
+1
+2
+3
+4
+5
+6
+7
–8
–7
–6
–5
–4
–3
–2
–1
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
+0
+1
+2
+3
+4
+5
+6
+7
–8
–7
–6
–5
–4
–3
–2
–1
0000
0111
0011
1011
1111
1110
1101
1100
1010
1001
1000
0110
0101
0100
0010
0001
Overflow conditions
  add two positive numbers to get a negative number
  add two negative numbers to get a positive number

## Slide 36: Overflow conditions
5
3
– 8
0 1 1 1 0 1 0 1 0 0 1 1 1 0 0 0
– 7
– 2
7
1 0 0 0 1 0 0 1 1 1 1 0 1 0 1 1 1
5
2
7
0 0 0 0 0 1 0 1 0 0 1 0 0 1 1 1
– 3
– 5
– 8
1 1 1 1 1 1 0 1 1 0 1 1 1 1 0 0 0
overflow
overflow
no overflow
no overflow
Overflow when carry into sign bit position is not equal to carry-out
The numbers in blue indicate carries into the next higher-order bits in calculation.
The condition to check overflow is to compare two highest carries in addition. If they are different, then it is an overflow.

## Slide 37: Circuits for binary addition
Ai Bi Sum Cout 0 0 0 0 0 1 1 0 1 0 1 0 1 1 0 1
Ai Bi Cin Sum Cout 0 0 0 0 0 0 0 1 1 0 0 1 0 1 0 0 1 1 0 1 1 0 0 1 0 1 0 1 0 1 1 1 0 0 1 1 1 1 1 1
Half adder (add 2 1-bit numbers)
  Sum = Ai' Bi + Ai Bi' = Ai xor Bi
  Cout = Ai Bi
Full adder (carry-in to cascade for multi-bit adders)
  Sum = Ci xor A xor B
  Cout = B Ci + A Ci + A B = Ci (A + B) + A B
Now we get familiar with 2s complement. Let’s design a circuit that adds two binary numbers. First of all, let’s start with a 1 bit adder. Ai and Bi are i-th bits of two binary numbers, A and B, respectively. On the left, there is a truth table for a half adder; on the right, a truth table for a full adder which also considers the carry-in from the lower-order bits.

## Slide 38: Full adder
Inputs: A, B, Carry-in
Outputs: Sum, Carry-out
A
B
Cin
Cout
S
A B Cin Cout S
0 0 0 0 0 1
0 1 0
0 1 1
1 0 0 1 0 1
1 1 0
1 1 1
0
1
1
0
1
0
0
1
0
0
0
1
0
1
1
1
Cout = A’ B Cin + A B’ Cin + A B Cin’ + A B Cin
S = A’ B’ Cin + A’ B Cin’ + A B’ Cin’ + A B Cin
A A A A A
B B B B B
S S S S S
Cin
Cout

## Slide 39: (A or B)C vs. (A xor B)C
A B C A+B (A+B)C 0 0 0 0 0 0 0 1 0 0 0 1 0 1 0 0 1 1 1 1 1 0 0 1 0 1 0 1 1 1 1 1 0 1 0 1 1 1 1 1
They are not equivalent but AB+(A+B)C = AB+(AB)C
Before going to the next step, let’s see the relation between two boolean expressions.
A B C AB (AB)C 0 0 0 0 0 0 0 1 0 0 0 1 0 1 0 0 1 1 1 1 1 0 0 1 0 1 0 1 1 1 1 1 0 0 0 1 1 1 0 0
(A or B)C is not equal to (A xor B)C. but when we add AB product term, they are equivalent.

## Slide 40: Full adder implementations
Cout = A B + Cin (A xor B) = A B + Cin (A or B)
A
B
Cin
S
A
A
B
B
Cin
Cout
A
B
A xor B
Cin
A xor B xor Cin
Half Adder
Sum
Cout
Cin (A xor B)
A B
Cout
Half Adder
Sum
Cout
At the top, there is a fixed logic implementation of a full adder. If we use two half-adder modules to construct the full-adder system instead of using random logic, we can reduce the number of gates.
Standard approach
  6 gates
  2 XORs, 2 ANDs, 2 ORs
Alternative implementation
  5 gates
  half adder is an XOR gate and AND gate
  2 XORs, 2 ANDs, 1 OR

## Slide 41: Adder/subtractor
Now we have a full adder for one bit addition. Then what we want to do is addition/subtraction of two 4bit-numbers. Addition is easy. Recall that 2s complement of a number is its inverted form+1. So we can use the same adding function to perform subtraction too. For subtraction, we just enable the control input.
A
B
Cout
Sum
Cin
0
1
Add' Subtract
A0
B0
B0'
Sel
Overflow
A
B
Cout
Sum
Cin
A1
B1
B1'
Sel
A
B
Cout
Sum
Cin
A2
B2
B2'
Sel
0
1
0
1
0
1
A
B
Cout
Sum
Cin
A3
B3
B3'
Sel
S3
S2
S1
S0
Use an adder to do subtraction thanks to 2s complement representation
  A – B = A + (– B) = A + B' + 1
  control signal selects B or 2s complement of B

## Slide 42: Ripple-carry adders
Critical delay
  the propagation of carry from low to high order stages
A
A
B
B
Cin
Cout
@0
@0
@0
@0
@N
@1
@1
@N+1
@N+2
late
arriving
signal
two gate delays
to compute Cout
4 stage
adder
A0
B0
0
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
The next advanced adder is a ripple-carry adder. What is the problem of the full adder in the previous slide? When we consider data bits, they are coming in parallel at the same time. However, carries should be cascaded with delays proportional to the bit positions. On the left, Cin comes at time N, then Cout will be valid at time N+2 (each one-bit adder incurs 2 gate delays)
1111+0001
A
B
Cin
S
@N
@N+1

## Slide 43: Why C1@2?
Worst-case delay of Cout = 3, but
  A=B=1 makes the delay 2 units
A
A
B
B
Cin
Cout
@0
@0
@0
@0
@N
@1
@1
@N+1
@N+2
late
arriving
signal
two gate delays
to compute Cout
4 stage
adder
A0
B0
0
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
1111+0001
A
B
Cin
S
@N
@N+1
1
1
0
1
2
1
1
0
1
1
1
2
1
1
Textbook 5.6.2

## Slide 44: Ripple-carry adders (cont’d)
Critical delay
  the propagation of carry from low to high order stages
  1111 + 0001 is the worst case addition
  carry must propagate through all bits
This slide shows a waveform of a 4 bit adder. Suppose we add 1111 and 0001, the carry will propagate from the LSB all the way through to the final carry-out.
4 stage
adder
A0
B0
0
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
1111+0001

## Slide 45: Carry-lookahead logic
Carry generate: Gi = Ai Bi
  must generate carry when A = B = 1
Carry propagate: Pi = Ai xor Bi
  carry-in will equal carry-out here
Sum and Cout can be re-expressed in terms of generate/propagate:
  Si = Ai xor Bi xor Ci = Pi xor Ci
  Ci+1 = Ai Bi + Ai Ci + Bi Ci = Ai Bi + Ci (Ai + Bi) = Ai Bi + Ci (Ai xor Bi) = Gi + Ci Pi
Instead of awaiting the carry from the lower-order bits, we can process the carry in advance. How?
In order to do so, the carry should be derived from the lower-order data bits directly. First of all, let’s look at two new functions: Gi and Pi. Then Si and Ci+1 can be rewritten as shown in the above. Actually, those imply two cases. When Gi is true, there is always a carry-out. If Pi is true, a carry-out depends on a carry-in.

## Slide 46: Carry-lookahead logic (cont’d)
Re-express the carry logic as follows:
  C1 = G0 + P0 C0
  C2 = G1 + P1 C1 = G1 + P1 G0 + P1 P0 C0
  C3 = G2 + P2 C2 = G2 + P2 G1 + P2 P1 G0 + P2 P1 P0 C0
  C4 = G3 + P3 C3 = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0 + P3 P2 P1 P0 C0
Each of the carry equations can be implemented with two-level logic
  all inputs are now directly derived from data inputs and not from intermediate carries
  this allows computation of all sum outputs to proceed in parallel
Then all the carries are calculated by the expanding Pi and Gi as shown in the above, which is called the carry-lookahead logic. Note that all carries are now just two-level logic functions. So here is the bottom line: there is a tradeoff between the number of gates and the delay.

## Slide 47: Carry-lookahead (CLA) implementation
G3
C0
C0
C0
C0
P0
P0
P0
P0
G0
G0
G0
G0
C1 @ 3
P1
P1
P1
P1
P1
P1
G1
G1
G1
C2 @ 3
P2
P2
P2
P2
P2
P2
G2
G2
C3 @ 3
P3
P3
P3
P3
C4 @ 3
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
increasingly complex logic for carries
Adder with propagate and generate outputs
This slide shows how 4 carries are implemented in two level fixed logic based on Pi and Gi. As Pi and Gi take only one gate delay, the final carries take maximum 3 gate delays.

## Slide 48: Building Blocks of Carry Lookahead Adder
G3
C0
C0
C0
C0
P0
P0
P0
P0
G0
G0
G0
G0
C1
P1
P1
P1
P1
P1
P1
G1
G1
G1
C2
P2
P2
P2
P2
P2
P2
G2
G2
C3
P3
P3
P3
P3
C4
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
1b Adder
Ai
Bi
Ci
Pi
Si
Gi
4b Carry Lookahead logic
C0
C1
P0
G0
P1
G1
P2
G2
P3
G3
C2
C3
C4
Assume all the inputs, A, B and C0 arrive at time 0. Unit gate delay.
For all i, delay of Pi, Gi = 1. Thus, delay of C1 = 2 + 1 = 3
Delay of C2 = 3, Delay of C3 = 3, Delay of C4 = 3  Delay of Ci = 3

## Slide 49: 4-bit Carry Lookahead Adder
1b Adder
A0
B0
C0
P0
S0
G0
4b Carry Lookahead logic
C0
C1
P0
G0
P1
G1
P2
G2
P3
G3
C2
C3
C4
1b Adder
A1
B1
C1
P1
S1
G1
1b Adder
A2
B2
C2
P2
S2
G2
1b Adder
A3
B3
C3
P3
S3
G3
4b Carry Lookahead Adder
C0
S0
A0
B0
S1
S2
S3
B1
B2
B3
A1
A2
A3
C4
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
Assuming A, B and C0 arrive at time 0
For all i >=1
Delay of Si = 1 + delay of Ci = 4

## Slide 50: CLA implementation (cont’d)
on the left, there is the original full adder, which takes a long time to finish addition. On the right, there is the carry lookahead adder. The two level logic functions for carries are not shown. Each box is the one-bit adder module. Overall, by using a lot of gates for CLA in the previous slide, we can reduce the delay of the addition process.
A0
B0
0
S0 @2
A1
B1
C1 @2
S1 @3
A2
B2
C2 @4
S2 @5
A3
B3
C3 @6
S3 @7
Cout @8
A0
B0
0
S0 @2
A1
B1
C1 @3
S1 @4
A2
B2
C2 @3
S2 @4
A3
B3
C3 @3
S3 @4
C4 @3
C4 @3
Carry-lookahead logic generates individual carries
  sums computed much more quickly in parallel
  however, cost of carry logic increases with more stages

## Slide 51: 16bit CLA adder with cascaded carry-lookahead logic
Carry-lookahead (CLA) adder
  4 four-bit adders with internal carry lookahead
  second level carry lookahead unit extends lookahead to 16 bits
If we add 16bit long numbers, we have to use 4 4bit CLA adder modules. Each module adds 4 bits. Here Ci at the bottom box is the carry from the i-th 4bit CLA adder module. Pi and Gi in blue color are the same functions in the previous example. While Pi and Gi at the bottom unit give info about the carries between the 4bit CLA modules, which is more complicated.
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@5
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
G = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0
P = P3 P2 P1 P0
C1 = G0 + P0 C0
C2 = G1 + P1 G0 + P1 P0 C0

## Slide 52: 16-bit Carry-Lookahead Adder
Group propagate and generate
  P = P0P1P2P3 (2 unit delay)
  G = G3 + G2P3 + G1P3P2 + G0P3P2P1 (3 unit delay)
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@5
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder

## Slide 53: 16-bit Carry-Lookahead Adder
2nd level lookahead carry logic
  Delay of C1 = 4
  Delay of C2, C3 and C4 = 5
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@5
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
3
2
4
3
2
2
2
5
3

## Slide 54: 16-bit Carry-Lookahead Adder
Delay of sum
  Delay of S[3-0] = 4
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@5
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder

## Slide 55: 4-bit Carry Lookahead Adder
1b Adder
A0
B0
C0
P0
S0
G0
4b Carry Lookahead logic
C0
C1
P0
G0
P1
G1
P2
G2
P3
G3
C2
C3
C4
1b Adder
A1
B1
C1
P1
S1
G1
1b Adder
A2
B2
C2
P2
S2
G2
1b Adder
A3
B3
C3
P3
S3
G3
4b Carry Lookahead Adder
C0
S0
A0
B0
S1
S2
S3
B1
B2
B3
A1
A2
A3
C4
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay
Assuming A, B and C0 arrive at time 0
For all i >=1
Delay of Si = 1 + delay of Ci = 4

## Slide 56: 16-bit Carry-Lookahead Adder
For the other sums, delay of sum = 3 + delay of Cin
  Delay of S[7-4] = 7
  Delay of S[11-8] and S[15-12] = 8
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@5
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder

## Slide 57: Carry-Lookahead Implementation
C0  Ci: 2 time units and Ci  Si: 1 time unit
Thus, C0  Si: 3 time units (Note: Ai and Bi arrive at time 0)
G3
C0
C0
C0
C0
P0
P0
P0
P0
G0
G0
G0
G0
C1
P1
P1
P1
P1
P1
P1
G1
G1
G1
C2
P2
P2
P2
P2
P2
P2
G2
G2
C3
P3
P3
P3
P3
C4
Pi @ 1 gate delay
Ci
Si @ 2 gate delays
Bi
Ai
Gi @ 1 gate delay

## Slide 58: 16bit CLA adder with cascaded carry-lookahead logic
Carry-lookahead (CLA) adder
  4 four-bit adders with internal carry lookahead
  second level carry lookahead unit extends lookahead to 16 bits
If we add 16bit long numbers, we have to use 4 4bit CLA adder modules. Each module adds 4 bits. Here Ci at the bottom box is the carry from the i-th 4bit CLA adder module. Pi and Gi in blue color are the same functions in the previous example. While Pi and Gi at the bottom unit give info about the carries between the 4bit CLA modules, which is more complicated.
Lookahead Carry Unit
C0
P0
G0
P1
G1
P2
G2
P3
G3
C3
C2
C1
C0
P3-0
G3-0
C4
@3
@2
@4
@3
@2
@5
@3
@2
@5
@3
@2
@5
@5
@3
@0
C16
A[15-12]
B[15-12]
C12
S[15-12]
A[11-8]
B[11-8]
C8
S[11-8]
A[7-4]
B[7-4]
C4
S[7-4]
@7
@8
@8
A[3-0]
B[3-0]
C0
S[3-0]
@0
@4
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
4
4
4
P
G
4-bit Adder
G = G3 + P3 G2 + P3 P2 G1 + P3 P2 P1 G0
P = P3 P2 P1 P0
C1 = G0 + P0 C0
C2 = G1 + P1 G0 + P1 P0 C0

## Slide 59: Carry-select adder
The next version, a carry-select adder, achieves even lower delay by redundant h/w. Note that the carry between 4bit CLA adders is either 0 or 1. We use two adder modules for high 4 bit of the 8-bit adder system. So we perform addition for both cases and then the carry from the lower 4bit CLA module will perform selection (MUX).
4-Bit Adder [3:0]
C0
C4
4-bit adder [7:4]
1
C8
0
C8
five 2:1 mux
0
1
0
1
0
1
0
1
adder low
adder high
0
1
4-bit adder [7:4]
C8
S7
S6
S5
S4
S3
S2
S1
S0
Redundant hardware to make carry calculation go faster
  compute two high-order sums in parallel while waiting for carry-in
  one assuming carry-in is 0 and another assuming carry-in is 1
  select correct result once carry-in is finally computed
@4
@3
@5

## Slide 60: Arithmetic logic unit (ALU) design specification
An ALU is a key subsystem of computers that performs logic and arithmetic functions. There are one high level control input M, and two lower level selection inputs S1 and S0. Here Ci is the carry value which is useful only for some arithmetic functions.
logical and arithmetic operations not all operations appear useful, but "fall out" of internal logic
S1 0 0 1 1
S0 0 1 0 1
Function Fi = Ai Fi = not Ai Fi = Ai xor Bi Fi = Ai xnor Bi
Comment input Ai transferred to output complement of Ai transferred to output compute XOR of Ai, Bi compute XNOR of Ai, Bi
M = 0, logical bitwise operations
M = 1, C0 = 0, arithmetic operations
0 0 1 1
0 1 0 1
F = A F = not A F = A plus B F = (not A) plus B
input A passed to output complement of A passed to output sum of A and B sum of B and complement of A
M = 1, C0 = 1, arithmetic operations
0 0 1 1
0 1 0 1
F = A plus 1 F = (not A) plus 1 F = A plus B plus 1 F = (not A) plus B plus 1
increment A twos complement of A increment sum of A and B B minus A

## Slide 61: Arithmetic logic unit (ALU) design (cont’d)
M 0 1 1
S1 0 0 1 1 0 0 1 1 0 0 1 1
S0 0 1 0 1 0 1 0 1 0 1 0 1
Ci X X X X X X X X X X X X 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1
Ai 0 1 0 1 0 0 1 1 0 0 1 1 0 1 0 1 0 0 1 1 0 0 1 1 0 1 0 1 0 0 1 1 0 0 1 1
Bi X X X X 0 1 0 1 0 1 0 1 X X X X 0 1 0 1 0 1 0 1 X X X X 0 1 0 1 0 1 0 1
Fi 0 1 1 0 0 1 1 0 1 0 0 1 0 1 1 0 0 1 1 0 1 0 0 1 1 0 0 1 1 0 0 1 0 1 1 0
Ci+1 X X X X X X X X X X X X X X X X 0 0 0 1 0 1 0 0 0 1 1 0 0 1 1 1 1 1 0 1
Sample ALU – truth table
First of all, there are three control inputs, three data inputs, and two data outputs.
If M is 0, Ci is a DC term. Sometimes, Bi is also a DC term when only the 1st input, Ai, matters

## Slide 62: ALU design (cont’d)
Sample ALU – multi-level discrete gate logic implementation
Total 12 gates + 5 inverters
\S1
\Bi
[35]
[35]
M
M
M
S1
Bi
[33]
[33]
[33]
[33]
S0
Ai
[30]
[30]
[30]
[30]
[30]
Ci
Ci
Ci
Ci
Co
\Co
\Co
\Co
\[30]
\[35]
Fi
If we implement the truth table in the previous slide by a random logic with some minimization techniques, we can get the above multi-level logic system. Don’t worry; there are six variables. Humans are not supposed to do that. This result comes from a CAD tool. Numbers in [] are internal wires.

## Slide 63: Summary for examples of combinational logic
Combinational logic design process
  formalize problem: encodings, truth-table, equations
  choose implementation technology (ROM, PAL, PLA, discrete gates)
  implement by following the design procedure for that technology
Binary number representation
  positive numbers the same
  difference is in how negative numbers are represented
  2s complement easiest to handle: one representation for zero, slightly complicated complementation, simple addition
Circuits for binary addition
  basic half-adder and full-adder
  carry lookahead logic
  carry-select
ALU Design
  specification, implementation
We looked at the design process of several combinational logic circuits and then reviewed how binary numbers are represented. Arithmetic functions are also discussed.